Wave Frequencies
# Result
The wave frequencies is a list of wave frequencies used in the analysis. This is the list of global wave frequencies. It does not consider body forward velocity or encounter angle. This essentially repeats back the frequencies the user input for the analysis. This output provides two useful things:
1. The frequency list confirms the inputs the user specified.
2. The frequency list shows the sequence of wave frequencies used. This sequence may be irregularly spaced, or there may be one or two special frequencies entered. That is why each individual frequency in the analysis is listed. This listing is important because oFreq will not list the wave frequencies in subsequent outputs. Each other output simply provides an ordered list. The sequence of the list of outputs matches the sequence of frequencies. Take the following example of wave frequencies (Table 1.1), and some generic output (Table 1.2).
Table 1.1: Wave Frequencies
0.005
0.010
0.300
0.500
0.700

Table 1.2: Generic Output
7.000
4.000
3.000
2.000
1.000

These tables show how the outputs will only provide a list of values. But the sequence of the list always matches the sequence of wave frequencies. So the output value of 7.000 occurs at a wave frequency of 0.005 rad/s. And the output value of 2.000 occurs at a wave frequency of 0.500 rad/s. The list of frequencies is the index for all other frequency based outputs.
## Units of Measurement
The wave frequencies are measured in radians per second (rad/s).
# Assumptions / Limitations
The output of wave frequencies makes the following simple assumptions.
At least one wave frequency was entered for the analysis.
# Variable Dependencies
The list of wave frequencies does not depend on any other variable in the analysis. It is an independent variable.
# Derivation
No derivation is necessary. The list of wave frequencies is an input provided by the user.
# Application to Custom Motion Models
The list of wave frequencies does not depend on the motion model selected. This output is always valid, regardless of the motion model.
# Response Amplitude Operator (RAO)
Most of the outputs are presented in two formats: the absolute value, and a response amplitude operator (RAO). The RAO gives the relative output for the given input. This can be useful when comparing the performance of the body on a general basis, independent of the given seastate. However, calculation of an RAO is not consistent through the industry or even from one input to the next. Section 6 addresses this by describing the exact calculation method of the RAO for each output.
## RAO Calculation
The RAO has no meaning for the global wave frequencies. No RAO is calculated.