Relative Efficiency
# Result
This output describes the relative efficiency of the body. The relative efficiency is a performance metric often used to assess device performance for wave energy extraction devices. It provides an indicator of how much power the device extracts from the sea, compared to the physical device size. First, oFreq calculates the capture width, and then uses the capture width to calculate relative efficiency.
The capture width compares power extracted to power input by the ocean waves. The user can define which forces contribute to the calculation of power extracted. (You can only select from the user defined forces.) oFreq takes the sum of average power extracted for all those forces. oFreq takes the power extracted by the body and divides by the power available per unit width of wave crest. This gives a width of wave crest that would be necessary to match the power extracted by the body. This term is called the capture width.
It is also useful to compare the capture width to a parameter of physical size on the body. This compares the returned power from the body to the investment and effort it took to construct the body. The user defines a parameter for the relevant physical width of the body. It is necessary for the user to define this parameter because the creativity of wave device concepts extends beyond physical parameters that oFreq can recognize. (Essentially, oFreq is not smart enough to interpret a device design.) The relative efficiency is the ratio of capture width to physical width defined by the user. This relative efficiency is frequently greater than 100%.
## Units of Measurement
The relative efficiency is unitless.
# Assumptions / Limitations
oFreq will only calculate extracted power for user defined forces. Hydrodynamic forces are not considered something that the body can extract power through. Rather, hydrodynamic forces impart power to the body.
# Variable Dependencies
The relative efficiency depends on the following elements.
1. The body selected.
2. Global wave frequency.
3. Global wave spectrum.
4. Global wave direction.
5. Body heading.
6. Influences of all reactive and active forces.
7. The motion model selected.
8. The capture width.
9. The specified physical width of the device.
# Derivation
The relative efficiency is the capture width, divided by the physical width of the body. (Equation 4.1)
%eta_r = %kappa over L_b
Equation 4.1
Variables:
%kappa = ~	Capture width.
Lb=	Relevant physical width of the body.

This relative efficiency is frequently greater than 100% and varies with body encountered frequency.
# Application to Custom Motion Models
The average power extracted gets calculated from the output for average power extracted. And the wave power available does not depend on the motion model. Because of this, the relative efficiency is accurate for any motion model specified, including any custom motion models.
# Response Amplitude Operator (RAO)
Most of the outputs are presented in two formats: the absolute value, and a response amplitude operator (RAO). The RAO gives the relative output for the given input. This can be useful when comparing the performance of the body on a general basis, independent of the given seastate. However, calculation of an RAO is not consistent through the industry or even from one input to the next. Section 6 addresses this by describing the exact calculation method of the RAO for each output.
## RAO Calculation
The RAO calculation is divided into two sections: first the RAO normalization is derived; and then the actual method of RAO application is shown. This may be specific to each RAO.
### RAO Normalization
The response amplitude operator is calculated through dividing the relative efficiency by the wave amplitude, calculated in the body coordinate system, using the body encounter spectrum. (Equation 6.1)
RAO(%eta_r) = %eta_r over %zeta_0b
Equation 6.1
Variables:
b =	Index of the body specified.
ηr =	Relative efficiency.
ζ0b =	Amplitude of the wave, in the body coordinate system.
### RAO Application
The RAO can be applied with simply multiplying by the wave amplitude. (Equation 6.2)
%eta_r = RAO(%eta_r) %zeta_ob
Equation 6.2
Variables:
b =	Index of the body specified.
RAO(%eta_r) = ~	Response amplitude operator to convert from incident wave amplitude, in the body coordinate system, over to the relative efficiency.
ζ0b =	Amplitude of the wave, in the body coordinate system.

Sometimes, it is more convenient to apply the RAO directly to the wave energy spectrum. There are two wave energy spectra to select from: the body encounter spectrum, and the global wave spectrum. Equation 6.3 shows application of the global wave spectrum. This includes application of an additional RAO to convert from the global wave spectrum to the body encounter spectrum. The output from this calculation is the spectral energy density of the relative efficiency.
S(%eta_r) = left ( RAO left ( %eta_r right ) right )^2 cdot left [ RAO(S(%omega_G)) cdot S(%omega_G) right ]
Equation 6.3
Variables:
RAO(%eta_r) = ~	Response amplitude operator to convert from incident wave amplitude, in the body coordinate system, over	to the capture width.
RAO(S(%omega_G)) = ~	RAO to convert from global wave spectrum to body encountered spectrum.
S(ωG) =	Global wave spectrum, spectral energy density.
## RAO Units
The units of the resulting RAO output can become very confusing, depending on how the RAO gets calculated. This section clarifies by clearly stating the units for each RAO.
The RAO for relative efficiency has units of m-1. (Equation 6.4)
left [ RAO(%eta_r) right ]_units = "%" over m = 1 over m = m^-1
Equation 6.4
Variables:
m =	Meters (m).