Absolute Efficiency
# Result
This output calculates the absolute efficiency, which is the power extracted by the body, compared to the theoretically maximum power extraction possible. The absolute efficiency is a performance metric often used to assess device performance for wave energy extraction devices. It provides an indicator of how much power the device extracts from the sea, compared to a theoretical maximum.
Power extracted by the device depends on which forces actually contribute to power extraction. The user can define which forces contribute to the calculation of power extracted. (You can only select from the user defined forces.) oFreq then takes the sum of average power extracted for all those forces. This forms the basis of comparison for absolute efficiency.
## Units of Measurement
The absolute efficiency is unitless.
# Assumptions / Limitations
oFreq will only calculate extracted power for user defined forces. Hydrodynamic forces are not considered something that the body can extract power through. Rather, hydrodynamic forces impart power to the body.
Calculation of relative efficiency depends on knowledge of the hydrodynamic damping coefficients. Consequently, the motion model selected must use some equation of motion that includes hydrodynamic forces. (Equation indices 1 through 6.)
# Variable Dependencies
The absolute efficiency depends on the following elements.
1. The body selected.
2. Global wave frequency.
3. Global wave spectrum.
4. Global wave direction.
5. Body heading.
6. Influences of all reactive and active forces.
7. The motion model selected.
8. The hydrodynamic damping coefficients for the body.
# Derivation
The theoretical maximum power was calculated from the hydrodynamic damping coefficient and forcing term at each frequency. (Equation 4.1)
overline {P_max} = 1 over 8 sum from v = 1 to 6 {{left lline F(v)_HydroActive right lline^2 } over {k(1,v)_HydroReact}}
Equation 4.1
Variables:
v =	Index of equation of motion.
F(v)HydroActive =	Hydrodynamic active force for equation of motion v.
k(1,v)HydroReact =	Coefficient of hydrodynamic reactive force for derivative 1, equation v, motion variable v.
Equation 4.1 is absolutely accurate to scenarios of a single degree of freedom system. However, it has not been verified for use in multiple degree of freedom systems. Or with use in a multi-body system. Use with caution. Later revisions will verify this equation. But for the moment, it is not the highest development priority.
The maximum power was calculated for each wave frequency and each equation of motion. The power from all equations of motion was added to give the total maximum power at each wave frequency. This forms the theoretical maximum power that could be extracted by the body at that wave frequency. Next, the actual power extracted at that frequency was divided by the total maximum power to give the absolute efficiency. (Equation 4.2)
%eta_a = bar P over overline {P_max}
Equation 4.2
Where:
P =	Total average power extracted by the body at a given body encounter frequency.
Pmax =	Maximum theoretical power than can be extracted from the body at the given body encounter frequency.

Values for absolute efficiency are usually very small (less than 50%).
# Application to Custom Motion Models
The absolute efficiency can be applied to nearly any motion model, including custom motion models.
The one requirement is that a motion model must include at least one equation of motion that references hydrodynamic coefficients (equations indices 1 through 6).
# Response Amplitude Operator (RAO)
Most of the outputs are presented in two formats: the absolute value, and a response amplitude operator (RAO). The RAO gives the relative output for the given input. This can be useful when comparing the performance of the body on a general basis, independent of the given seastate. However, calculation of an RAO is not consistent through the industry or even from one input to the next. Section 6 addresses this by describing the exact calculation method of the RAO for each output.
## RAO Calculation
The RAO calculation is divided into two sections: first the RAO normalization is derived; and then the actual method of RAO application is shown. This may be specific to each RAO.
### RAO Normalization
The response amplitude operator is calculated through dividing the absolute efficiency by the wave amplitude, calculated in the body coordinate system, using the body encounter spectrum. (Equation 6.1)
RAO(%eta_a) = %eta_a over %zeta_0b
Equation 6.1
Variables:
b =	Index of the body specified.
ηa =	Absolute efficiency.
ζ0b =	Amplitude of the wave, in the body coordinate system.
### RAO Application
The RAO can be applied with simply multiplying by the wave amplitude.
%eta_a = RAO(%eta_a) %zeta_ob
Equation 6.2
Variables:
b =	Index of the body specified.
RAO(ηa) =	Response amplitude operator to convert from incident wave amplitude, in the body coordinate system, over to the absolute efficiency.
ζ0b =	Amplitude of the wave, in the body coordinate system.

Sometimes, it is more convenient to apply the RAO directly to the wave energy spectrum. There are two wave energy spectra to select from: the body encounter spectrum, and the global wave spectrum. Equation 6.3 shows application of the global wave spectrum. This includes application of an additional RAO to convert from the global wave spectrum to the body encounter spectrum. The output from this calculation is the spectral energy density of the absolute efficiency.
S(%eta_a) = left ( RAO left ( %eta_a right ) right )^2 cdot left [ RAO(S(%omega_G)) cdot S(%omega_G) right ]
Equation 6.3
Variables:
RAO(ηa) =	Response amplitude operator to convert from incident wave amplitude, in the body coordinate system, over	to the absolute efficiency.
RAO(S(%omega_G)) = ~	RAO to convert from global wave spectrum to body encountered spectrum.
S(ωG) =	Global wave spectrum, spectral energy density.
## RAO Units
The units of the resulting RAO output can become very confusing, depending on how the RAO gets calculated. This section clarifies by clearly stating the units for each RAO.
The RAO for absolute efficiency has units of m-1. (Equation 6.4)
left [ RAO(%eta_a) right ]_units = "%" over m = 1 over m = m^-1
Equation 6.4
Variables:
m =	Meters (m).