Body Motion Derivative
# Result
This output provides information about the body motions. It presents the value of the derivative for each motion variable, detailed for each wave frequency specified. The user specifies the order of the derivative. oFreq also calculates the derivative values for standard desired derivatives (motion, velocity, and acceleration). However the user may have need to know body motions for higher order derivatives (possibly for designing a control system). The user can specify any order of derivative, and oFreq will present the output, giving results for each variable of motion.
## Units of Measurement
The units of measurement depend on the variable of motion and the order of derivative specified. The following formula may be used to calculate the units of the output.
units = X / s^N
Equation 1.1
Variables:
X =	Units of the motion variable in question (determined by the motion model).
s =	Units of seconds (s).
N =	Order of derivative requested by the user.
# Assumptions / Limitations
This output assumes an oscillatory motion at a steady state value. Transient effects are ignored.
# Variable Dependencies
This output depends on the following variables.
1. Body encounter frequency.
2. Global wave direction.
3. Body heading.
4. All the body input forces
5. Global wave spectrum
6. Requested order of derivative for output.
# Derivation
Equation 4.1 shows the calculation of any derivative of body variables. This equation assumes the body motion variables are already solved.
{d^i underline X_v} over {d t^i} = left ( j %omega_b right )^i underline X_v
Equation 4.1
Variables:
v =	Index of the body motion variable in question (numbered starting from 1).
i =	Order of derivative requested.
Xv =	Amplitude of body motion variable, index v.
j =	Imaginary number.
ωb =	Body encounter frequency.
Underline notation denotes a complex variable.

The calculation of any derivative for the body motion derivative depends on the body encounter frequency, and not the global wave frequency.
Although derivatives of body motion are calculated based on body encounter frequency, they can still be compared to the global wave frequency. The dependency is a valid comparison.
But do not extend this concept to the response amplitude operators. The calculation of the RAO depends on the exact encountered wave spectrum and can not be generalized to the global wave frequency.
# Application to Custom Motion Models
This output is flexible enough to accommodate all motion models, including custom motion models. It will accurately report the requested derivative of body motions for any motion model used.
# Response Amplitude Operator (RAO)
Most of the outputs are presented in two formats: the absolute value, and a response amplitude operator (RAO). The RAO gives the relative output for the given input. This can be useful when comparing the performance of the body on a general basis, independent of the given seastate. However, calculation of an RAO is not consistent through the industry or even from one input to the next. Section 6 addresses this by describing the exact calculation method of the RAO for each output.
## RAO Calculation
The RAO calculation is divided into two sections: first the RAO normalization is derived; and then the actual method of RAO application is shown. This may be specific to each RAO.
### RAO Normalization
For all motions, the RAO is normalized based on wave amplitude for the given body encounter spectrum. (Equation 6.1)
The original motions were a complex variable, which tracked the magnitude of the response and it phase angle relative to the incident wave. However, RAO's are often used to quickly generalize a set of results and apply them to another situation. In that case, the phase angle of the force might not be accurate to the next situation. So only the magnitude of the RAO is reported. This provided a worst case scenario.
In reality, the difference in phase angles mean that the maximum motions never occur at that same time. The real motion will always be less than the magnitude reported through the RAO. But the exact quantity can not be accurately reported through application of an RAO. The conservative approach was to only report the magnitude.
RAO left ( {d^i X_v} over {d t^i} right ) = left ldline left ({d^i underline X_v} over {d t^i} right ) over %zeta_0b right ldline
Equation 6.1
Variables:
left ( {d^i underline X_v} over {d t^i} right ) = ~	Requested derivative of body motion for the body of index b.
ζ0b =	Encountered wave amplitude for the body of index b.
b =	Index of body specified.
Underline notation denotes a complex variable.

### RAO Application
The RAO can be applied with simply multiplying by the wave amplitude.
left ({d^i X_v} over {d t^i} right ) = RAO left ( {d^i X_v} over {d t^i} right ) ` %zeta_0b
Equation 6.2
Variables:
ζ0b =	Encountered wave amplitude for the body of index b.
b =	Index of body specified.

Sometimes, it is more convenient to apply the RAO directly to the wave energy spectrum. There are two wave energy spectra to select from: the body encounter spectrum, and the global wave spectrum. Equation 6.3 shows application of the global wave spectrum. This includes application of an additional RAO to convert from the global wave spectrum to the body encounter spectrum. The output from this calculation is the spectral energy density of the requested derivative of the body motion.
S left ({d^i X_v} over {d t^i} right ) = left ( RAO left ( {d^i X_v} over {d t^i} right ) right )^2 cdot left [ RAO(S(%omega_G)) cdot S(%omega_G) right ]
Equation 6.3
Variables:
RAO left ( {d^i X_v} over {d t^i} right ) = ~	Response amplitude operator (RAO) to convert from body wave amplitude to body motion derivative.
RAO(S(%omega_G)) = ~	RAO to convert from global wave spectrum to body encountered spectrum.
S(ωG) =	Global wave spectrum, spectral energy density.

## RAO Units
The units of the resulting RAO output can become very confusing, depending on how the RAO gets calculated. This section clarifies by clearly stating the units for each RAO.
The units of the RAO depend on the motion model, motion variable, and order of derivative requested. Equation 6.4 provides the formula to determine the units for the RAO of the output.
left [ RAO left ( {d^i X_v} over {d t^i} right ) right ]_units = X over {m s^N}
Equation 6.4
Variables:
X =	Units of the motion variable in question (determined by the motion model).
m =	Units of meters (m).
s =	Units of seconds (s).
N =	Order of derivative requested by the user.