Local Dynamic Freeboard
# Result
This output provides the components of a solution at a local point on the ship, converted into translation components. The body solution may include elements of both translation and rotation within its equations of motion. Due to differences in phase angles, these elements combine in complex ways to form different resultant motions at local points on the ship. This output combines the rotation and translation components to resolve a single motion, composed of only three translation components at some user defined position.
When oFreq calculates the output, it accounts for relative phase angles between all the body motions. The phase angles for body motions change depending on body encounter frequency. Because of this, the local solution is a linear function with respect to its physical position on the body, but non-linear with body encounter frequency.
The local dynamic freeboard is similar to calculation of the local motion, but this subtracts the elevation of the wave at that local point. The result details the distance from the local point to the top of the water surface, accounting for the wave present. A negative freeboard indicates that the local point is under water and the body has green water on deck.
oFreq only calculate the dynamic freeboard for individual waves at a fixed frequency. It does not consider the combined effect of wave combinations, as you find in real seaways. However, this output does present sufficient data for a statistical analysis of a real seaway. (The statistical analysis is not covered within this documentation for oFreq.)
## Units of Measurement
The local motion has units of meters (m).
# Assumptions / Limitations
This output makes the following assumptions.
1. This outputs assumes rigid body motion.
2. This output assumes an oscillatory motion at a steady state value. Transient effects are ignored.
3. This output assumes a standard six degree of freedom motion model (6DOF). The output will still calculate if not all of the 6DOF variables are included, but that will affect the final solution. And the output can not consider any motion variables that extend beyond rigid body motion (the reserved variables of 1 – 6).
4. Body motions are defined from the origin of the body coordinate system.
5. The coordinates of the local point of output are known and resolved within the body coordinate system.
# Variable Dependencies
This output depends on the following variables.
1. Body encounter frequency.
2. Global wave direction.
3. Body heading.
4. All the body input forces
5. Global wave spectrum
6. Position specified for the local solution.
# Derivation
The body motion variables are first converted into the local motion variables. Equation 4.1 resolves the dynamic freeboard, in the body coordinate system. All equations assume the solution for the body motion variables is known.
underline s_{3 %zeta} = underline x_3 + r_by underline x_4 + r_bx underline x_5 - underline %zeta_b
Equation 4.1
Variables:
s3 =	Local translation motion on the Z-axis, in the body coordinate system.
x3 =	Body motion variable, translation on the Z-axis, in the body coordinate system.
x4 =	Body motion variable, rotation about the X-axis, in the body coordinate system.
x5 =	Body motion variable, rotation about the Y-axis, in the body coordinate system.
rbx =	Position of the local solution point, X-axis coordinate.
rby =	Position of the local solution point, Y-axis coordinate.
ζ =	Wave elevation, body coordinate system.
underline notation denotes a complex number.

Notice that the variable for wave elevation also includes the phase angle. This phase angle accounts for the relative timing between the body motions and the wave crest. The phase angle should be defined as zero, because all other motions are measured relative to the incident wave. All the other motions will likely have non-zero phase angles, which accounts for the relative timing between incident wave crest and body motions.
The resulting variable for dynamic freeboard is also a complex variable. This tracks the magnitude and phase angle of the resulting dynamic freeboard at any given point in time. To find the actual value of dynamic freeboard for a specific point in time, first calculate Equation 4.1 and then take the real value of the result.
The calculation of the local motion depends on the body encounter frequency, and not the global wave frequency.
Although the local dynamic freeboard is based on body encounter frequency, it can still be compared to the global wave frequency. The dependency is a valid comparison.
But do not extend this concept to the response amplitude operators. The calculation of the RAO depends on the exact encountered wave spectrum and can not be generalized to the global wave frequency.
# Application to Custom Motion Models
This output assumes a standard six degree of freedom motion model (6DOF). The output will still calculate if not all of the 6DOF variables are included, but that will affect the final solution. And the output can not consider any motion variables that extend beyond rigid body motion (the reserved variables of 1 – 6).
This output will still work with custom motion models, but it can only access information for motion variables 1 – 6. These outputs are reserved for rigid body motions. If you require local solution information that includes the effects of other custom motion variables, this output will not return an accurate solution. Consider developing a custom output.
# Response Amplitude Operator (RAO)
Most of the outputs are presented in two formats: the absolute value, and a response amplitude operator (RAO). The RAO gives the relative output for the given input. This can be useful when comparing the performance of the body on a general basis, independent of the given seastate. However, calculation of an RAO is not consistent through the industry or even from one input to the next. Section 6 addresses this by describing the exact calculation method of the RAO for each output.
## RAO Calculation
The RAO calculation is divided into two sections: first the RAO normalization is derived; and then the actual method of RAO application is shown. This may be specific to each RAO.
### RAO Normalization
For all local solution variables, the RAO is normalized based on wave amplitude for the given body encounter spectrum. (Equation 6.1)
The original local solution variables were a complex variable, which tracked the magnitude of the response and it phase angle relative to the incident wave. However, RAO's are often used to quickly generalize a set of results and apply them to another situation. In that case, the phase angle of the force might not be accurate to the next situation. So only the magnitude of the RAO is reported. This provided a worst case scenario.
In reality, the difference in phase angles mean that the maximum motions never occur at that same time. The real motion will always be less than the magnitude reported through the RAO. But the exact quantity can not be accurately reported through application of an RAO. The conservative approach was to only report the magnitude.
RAO left ( S_{3 %zeta} right ) = left ldline underline S_{3 %zeta} over %zeta_0b right ldline
Equation 6.1
Variables:
S3ζ =	Amplitude of response for local dynamic freeboard.
ζ0b =	Encountered wave amplitude for the body of index b.
b =	Index of body specified.
Underline notation denotes a complex variable.

### RAO Application
The RAO can be applied with simply multiplying by the wave amplitude.
S_{3 %zeta} = RAO left ( S_{3 %zeta} right ) ` %zeta_0b
Equation 6.2
Variables:
ζ0b =	Encountered wave amplitude for the body of index b.
b =	Index of body specified.
RAO left ( S_{3 %zeta} right ) = ~	Response amplitude operator (RAO) to convert from body wave amplitude to local dynamic freeboard.

Sometimes, it is more convenient to apply the RAO directly to the wave energy spectrum. There are two wave energy spectra to select from: the body encounter spectrum, and the global wave spectrum. Equation 6.3 shows application of the global wave spectrum. This includes application of an additional RAO to convert from the global wave spectrum to the body encounter spectrum. The output from this calculation is the spectral energy density of the motion of the local solution.
S left (S_{3 %zeta} right ) = left ( RAO left ( S_{3 %zeta} right ) right )^2 cdot left [ RAO(S(%omega_G)) cdot S(%omega_G) right ]
Equation 6.3
Variables:
RAO left ( S_{3 %zeta} right ) = ~	Response amplitude operator (RAO) to convert from body wave amplitude to local dynamic freeboard.
RAO(S(%omega_G)) = ~	RAO to convert from global wave spectrum to body encountered spectrum.
S(ωG) =	Global wave spectrum, spectral energy density.
## RAO Units
The units of the resulting RAO output can become very confusing, depending on how the RAO gets calculated. This section clarifies by clearly stating the units for each RAO.
The RAO for local dynamic freeboard is unitless.
left [ RAO left ( S_{3 %zeta} right ) right ]_units = m over m = unitless
Equation 6.4
Variables:
m =	Meters (m)