Local Design Acceleration
# Result
This output provides the components of a solution at a local point on the ship, converted into translation components. The body solution may include elements of both translation and rotation within its equations of motion. Due to differences in phase angles, these elements combine in complex ways to form different resultant motions at local points on the ship. This output combines the rotation and translation components to resolve a single motion, composed of only three translation components at some user defined position.
When oFreq calculates the output, it accounts for relative phase angles between all the body motions. The phase angles for body motions change depending on body encounter frequency. Because of this, the local solution is a linear function with respect to its physical position on the body, but non-linear with body encounter frequency.
First, oFreq calculates the local motion at the point specified, and then it calculates the acceleration of the solution at that point.
For the design acceleration, oFreq also includes the acceleration from static gravity at extreme motions (static acceleration). The design acceleration accounts for the phase angles between static acceleration and dynamic acceleration.
## Units of Measurement
The units of measurement are meters per second squared (m/s2).
units = m / s^2
Equation 1.1
Variables:
m =	Units of meters (m).
s =	Units of seconds (s).
# Assumptions / Limitations
This output makes the following assumptions.
1. This outputs assumes rigid body motion.
2. This output assumes an oscillatory motion at a steady state value. Transient effects are ignored.
3. This output assumes a standard six degree of freedom motion model (6DOF). The output will still calculate if not all of the 6DOF variables are included, but that will affect the final solution. And the output can not consider any motion variables that extend beyond rigid body motion (the reserved variables of 1 – 6).
4. Body motions are defined from the origin of the body coordinate system.
5. The coordinates of the local point of output are known and resolved within the body coordinate system.
# Variable Dependencies
This output depends on the following variables.
1. Body encounter frequency.
2. Global wave direction.
3. Body heading.
4. All the body input forces
5. Global wave spectrum
6. Position specified for the local solution.
# Derivation
## Dynamic Acceleration Calculation
oFreq first calculates the dynamic acceleration at the local point specified. This used the methods described in T04-0050.0023. It produced the following three variables for local linear acceleration for any specified point on the body.
Equation 4.1 gives the dynamic acceleration along the X-axis, in the body coordinate system.
{d^2 underline S_x} over {d t^2}
Equation 4.1
Error: Reference source not found gives the dynamic acceleration along the Y-axis, in the body coordinate system.
{d^2 underline S_y} over {d t^2}
Equation 4.2
Error: Reference source not found gives the dynamic acceleration along the Z-axis, in the body coordinate system.
{d^2 underline S_z} over {d t^2}
Equation 4.3
All variables were complex variables.
## Static Acceleration Calculation
The static acceleration was calculated using the methods described in T04-0050.0014. The following variables were defined.
Variables:
ax =	Maximum static acceleration in the X-axis, body coordinate system.
ay =	Maximum static acceleration in the Y-axis, body coordinate system.
az =	Minimum static acceleration in the Z-axis, body coordinate system.
underline notation denotes complex variables.

## Combined Design Acceleration
The static and dynamic acceleration were combined to yield the final design acceleration.
Error: Reference source not found gives the design acceleration in the X-axis, body coordinate system.
underline a_dx = {d^2 underline S_x} over {dt^2} + underline a_x
Equation 4.4
Error: Reference source not found gives the design acceleration in the Y-axis, body coordinate system.
underline a_dy = {d^2 underline S_y} over {dt^2} - underline a_y
Equation 4.5
Error: Reference source not found gives the design acceleration in the Z-axis, body coordinate system.
underline a_dz = {d^2 underline S_z} over {dt^2} + underline a_z
Equation 4.6
Although acceleration of the local solution is calculated based on body encounter frequency, it can still be compared to the global wave frequency. The dependency is a valid comparison.
But do not extend this concept to the response amplitude operators. The calculation of the RAO depends on the exact encountered wave spectrum and can not be generalized to the global wave frequency.
# Application to Custom Motion Models
This output assumes a standard six degree of freedom motion model (6DOF). The output will still calculate if not all of the 6DOF variables are included, but that will affect the final solution. And the output can not consider any motion variables that extend beyond rigid body motion (the reserved variables of 1 – 6).
This output will still work with custom motion models, but it can only access information for motion variables 1 – 6. These outputs are reserved for rigid body motions. If you require local solution information that includes the effects of other custom motion variables, this output will not return an accurate solution. Consider developing a custom output.
# Response Amplitude Operator (RAO)
Most of the outputs are presented in two formats: the absolute value, and a response amplitude operator (RAO). The RAO gives the relative output for the given input. This can be useful when comparing the performance of the body on a general basis, independent of the given seastate. However, calculation of an RAO is not consistent through the industry or even from one input to the next. Section 6 addresses this by describing the exact calculation method of the RAO for each output.
## RAO Calculation
The RAO calculation is divided into two sections: first the RAO normalization is derived; and then the actual method of RAO application is shown. This may be specific to each RAO.
### RAO Normalization
For all design acceleration variables, the RAO is normalized based on wave amplitude for the given body encounter spectrum. (Equation 6.1)
The original design acceleration variables were a complex variable, which tracked the magnitude of the response and it phase angle relative to the incident wave. However, RAO's are often used to quickly generalize a set of results and apply them to another situation. In that case, the phase angle of the force might not be accurate to the next situation. So only the magnitude of the RAO is reported. This provided a worst case scenario.
In reality, the difference in phase angles mean that the maximum motions never occur at that same time. The real motion will always be less than the magnitude reported through the RAO. But the exact quantity can not be accurately reported through application of an RAO. The conservative approach was to only report the magnitude.
RAO left ( a_dv right ) = left ldline underline a_dv over %zeta_0b right ldline
Equation 6.1
Variables:
adv =	Design acceleration for the index v requested.
ζ0b =	Encountered wave amplitude for the body of index b.
b =	Index of body specified.
v =	Index of the local motion component requested (1 – 3, 1 = x, 2 = y, 3 = z).
Underline notation denotes a complex variable.

### RAO Application
The RAO can be applied with simply multiplying by the wave amplitude.
a_dv = RAO left ( a_dv right ) ` %zeta_0b
Equation 6.2
Variables:
ζ0b =	Encountered wave amplitude for the body of index b.
v =	Index of the local motion component requested (1 – 3, 1 = x, 2 = y, 3 = z).
b =	Index of body specified.
RAO(adv) =	Response amplitude operator (RAO) to convert from body wave amplitude to local design acceleration, for component v.

Sometimes, it is more convenient to apply the RAO directly to the wave energy spectrum. There are two wave energy spectra to select from: the body encounter spectrum, and the global wave spectrum. Equation 6.3 shows application of the global wave spectrum. This includes application of an additional RAO to convert from the global wave spectrum to the body encounter spectrum. The output from this calculation is the spectral energy density for the local design acceleration.
S left ( a_dv right ) = RAO left ( a_dv right )^2 cdot left [ RAO(S(%omega_G)) cdot S(%omega_G) right ]
Equation 6.3
Variables:
RAO(adv) =	Response amplitude operator (RAO) to convert from body wave amplitude to local design acceleration, for component v.
RAO(S(%omega_G)) = ~	RAO to convert from global wave spectrum to body encountered spectrum.
S(ωG) =	Global wave spectrum, spectral energy density.
## RAO Units
The units of the resulting RAO output can become very confusing, depending on how the RAO gets calculated. This section clarifies by clearly stating the units for each RAO.
The units for acceleration of the local solution are s-2. (Equation 6.4)
left [ RAO left ( a_dv right ) right ]_units = m over {m s^2} = 1 over s^2 = s^-2
Equation 6.4
Variables:
m =	Units of meters (m).
s =	Units of seconds (s).