Average Power Extraction
# Result
This output calculates the average rate of power extraction for a specified body force. This only applies to reactive forces or crossbody forces. Active forces do not extract power. Here force is generic term and can mean either a translation force or a rotation moment, depending on the equation of motion.
The power output is calculated for each defined force term. The calculation calculates the total power extraction from all derivatives and all motion variables defined as inputs for the force object. oFreq will provide details of power extracted for each equation of motion defined within a force object. It will also report the total of all equations of motion within the force object. For example, if a reactive force included influences from equations for x1, x2, and x3, then oFreq would report three power extraction terms for that force, one for each equation. oFreq would also report a total that was the sum of the previous three terms.
oFreq will report a result for every reactive force defined in the analysis. This includes hydrodynamic forces automatically defined by inclusion of a hydrodynamic body. The reactive force from body mass is also included in the output. oFreq considers each force definition to be its own object. Output information is organized with the same structure that the forces were defined in the analysis.
When defining the force objects in oFreq, consider what level of detail you want when oFreq reports the outputs. For example, if you want to separate out the influence of individual variables within a single physical force, you must define it as two separate force objects in oFreq. That way oFreq can evaluate the influence separately.

“Average” for this output means the power extracted, when averaged across one wave period for the defined body encountered frequencies. It is not an average across multiple body encounter frequencies.
## Units of Measurement
The output has units of Watts.
units = Watts = N-m over s
Equation 1.1
# Assumptions / Limitations
The physics mean that oFreq will calculate zero power extracted for any even numbered derivative. These derivatives are in perfect synchronization with the generated motions and no power is extracted. This means that power outputs for some force terms (such as the mass force term) will always be zero, due to the physics. The user can rely on these properties to double check the output and ensure oFreq operates correctly.
# Variable Dependencies
The average extracted power depends on the following elements.
1. The body selected.
2. Global wave frequency.
3. Global wave spectrum.
4. Global wave direction.
5. Body heading.
6. Influences of all reactive and active forces.
7. The motion model selected.
# Derivation
The interactions of the various derivatives can become slightly complicated for this output. To address the complexity, the full derivation for the output is presented. The final formula is relatively simple, but the mathematical proof of its validity is not immediately apparent without the full derivation.
In the following equations, the force coefficients are references (k(u,v) terms). These are slightly different from the input coefficients. oFreq requests the force coefficients from the motion model for that body. This request allows the motion model to include any fixed constants that are not defined as part of the force.
The following equations do assume the motion variables are solved.
The following equations are not specific to any one force type. They can be applied to any of the following force types:
1. User reactive force
2. Hydrodynamic reactive force
3. User crossbody force
4. Hydrodynamic crossbody force
5. Mass force.
Application to the crossbody force does require an additional summation term that is shown later, in Section 4.1.
To derive the average power extracted, start with a simple generic definition for the power extraction. (Equation 4.1)
bar P = 1 over T int from 0 to T F_v(t) cdot dot x_v(t) dt
Equation 4.1
Variables:
T =	Period of measurement
Fv(t) =	Force function (including time variation) for index v.
v =	Index of motion variable.
dot x_v(t) = ~	Velocity of motion variable for index v.

Equation 4.1 can be applied to the calculations of oFreq with the following variable definitions. Equation 4.2 defines the period used to average the power calculation.
T = {2 %pi} over %omega_b
Equation 4.2
Variables:
ωb =	Body encounter frequency.

Equation 4.3 defines the body force, using the force definitions in oFreq. The equation assumes the body motion variable is already solved. This force definition is actually just for a single equation of a force definition. The concept can be applied to each equation of motion.
F_v(t) = sum from u = 0 to N sum from v = 1 to Q k(u,v) %omega_b^u X_v Re left lbrace j^u exp left [ j left ( %omega_b t + %delta_v right ) right ] right rbrace
Equation 4.3
Subscripts:
u =	Order of derivative.
v =	Motion variable.
N =	Maximum order of derivative.
Q =	Maximum number of variables of motion.

Variables:
k(u,v) =	Force coefficient for derivative u, motion variable v (obtained through evaluation of the motion model).
ωb =	Body encounter frequency.
Xv =	Amplitude of body motion.
j =	Imaginary number.
t =	Time.
δv =	Phase angle of solved body motion for motion variable v.

Equation 4.4 defines the velocity of the motion variable.
dot x_v(t) = %omega_b X_v Re left lbrace j exp left [ j left ( %omega_b t + %delta_v right ) right ] right rbrace
Equation 4.4

Subscripts:
v =	Motion variable.

Variables:
ωb =	Body encounter frequency.
Xv =	Amplitude of body motion.
j =	Imaginary number.
t =	Time.
δv =	Phase angle of solved body motion for motion variable v.

Simplification of Equation 4.3 follows two possible routes, depending on whether the order of derivative (subscript u) is an even or odd value. Odd values of u will produce non trivial solutions. Even values will always produce an average power extraction of zero. The derivation proceeds forward assuming only odd values for the subscript u.
Calculation of average power requires taking the real values of both force and velocity, before multiplying the two terms together. Equation 4.5 shows the force term, evaluated for real values only.
F_v(t) = sum from u = 0 to N sum from v = 1 to Q k(u,v) %omega_b^u X_v Re left lbrace j^u exp left [ j left ( %omega_b t + %delta_v right ) right ] right rbrace ~drarrow newline newline F_v(t) = sum from u = 0 to N sum from v = 1 to Q k(u,v) %omega_b^u X_v left ( -1 right )^{{u-1} over 2} Re left lbrace j cos (%omega_b t + %delta_v) - sin(%omega_b t + %delta_v) right rbrace ~drarrow newline newline F_v(t) = sum from u = 0 to N sum from v = 1 to Q k(u,v) %omega_b^u X_v left ( -1 right )^{{u-1} over 2} left (-1 right ) sin(%omega_b t + %delta_v) ~drarrow newline newline F_v(t) = sum from u = 0 to N sum from v = 1 to Q k(u,v) %omega_b^u X_v left ( -1 right )^{{u+1} over 2} sin(%omega_b t + %delta_v)
Equation 4.5

Equation 4.6 shows evaluation of the velocity variable for the real component.
dot x_v(t) = %omega_b X_v Re left lbrace j exp left [ j left ( %omega_b t + %delta_v right ) right ] right rbrace ~ drarrow newline newline dot x_v(t) = %omega_b X_v Re left lbrace j cos( %omega_b t + %delta_v) - sin(%omega_b t + %delta_v) right rbrace ~ drarrow newline newline dot x_v(t) = - %omega_b X_v sin(%omega_b t + %delta_v)
Equation 4.6
Equation 4.5 and Equation 4.6are now combined in Equation 4.7 to continue the derivation for average power extracted.

bar P = %omega_b over {2 %pi} int from 0 to {2 %pi over %omega_b} F_v(t) cdot dot x_v(t) dt ~ drarrow newline newline bar P = %omega_b over {2 %pi} sum from stack { u = 0 # odd} to N sum from v = 1 to Q left ( -1 right ) ^{{u+1} over 2} left ( -1 right ) k(u,v) %omega_b^{u+1} X_v^2 int from 0 to {2 %pi over %omega_b} sin^2 ( %omega_b t + %delta_v ) dt ~ drarrow newline newline bar P = %omega_b over {2 %pi} sum from stack { u = 0 # odd} to N sum from v = 1 to Q left ( -1 right ) ^{{u+3} over 2} k(u,v) %omega_b^{u+1} X_v^2 int from 0 to {2 %pi over %omega_b} sin^2 ( %omega_b t + %delta_v ) dt ~ drarrow newline newline
Equation 4.7

The next equations focus on evaluation of the integral. Integral evaluation requires a frew trigonometric identities, which are shown in Equation 4.8.
matrix { sin^2 (A) + cos^2(A) = 1 # ~ # (TrigA) ## 2 cos(A) cos(B) = cos(A - B) + cos(A + B) # ~ # (TrigB) ## cos(A +- B) = cos(A) cos(B) -+ sin(A) sin(B) # ~ # (TrigC) }
Equation 4.8
Equation 4.9 shows evaluation of the integral. The specific trigonometric identities are also indicated.
matrix { int from 0 to {{2 %pi} over %omega_b} sin^2 (%omega_b t + %delta_v) dt ~drarrow # ~ # (TrigA) ## int from 0 to {{2 %pi} over %omega_b} 1 - cos^2 (%omega_b t + %delta_v) dt ~drarrow # ~ # (TrigB) ## int from 0 to {{2 %pi} over %omega_b} 1 - 1 over 2 + {cos (2 %omega_b t + 2 %delta_v)} over 2 dt ~drarrow # ~ # (TrigB) ## left [ t over 2 right ] _0 ^ {{2 %pi} over %omega_b} + int from 0 to {{2 %pi} over %omega_b} {{cos (2 %omega_b t + 2 %delta_v)} over 2} dt ~drarrow # ~ # (Evaluate Integral) ## %pi over %omega_b + 0 ~drarrow # ~ # ~ ## %pi over %omega_b # ~ # ~ }
Equation 4.9
The evaluated integral was reintroduced to the main equation. A little further simplification reveals the final equation to calculate average power extraction for reactive forces as defined in oFreq. (Equation 4.10)
bar P = 1 over 2 sum from stack { u = 0 # odd } to N sum from v = 1 to Q left ( -1 right )^ {{u + 3} over 2} X_v^2 %omega_b^{u+1} k(u,v)
Equation 4.10
Subscripts:
u =	Order of derivative.
v =	Motion variable.
N =	Maximum order of derivative.
Q =	Maximum number of variables of motion.

Variables:
k(u,v) =	Force coefficient for derivative u, motion variable v (obtained through evaluation of the motion model).
ωb =	Body encounter frequency.
Xv =	Amplitude of body motion.
j =	Imaginary number.

This expression should work for all reactive forces.
## Application to Crossbody Forces
Equation 4.10 must be modified slightly for application to crossbody forces. It must included an additional summation term to include motions from all sending bodies. And the body encounter frequency must be modified to consider the encounter frequency of the other bodies. The following formula assumes calculation of average extracted power for body 1. That is, body 1 receives the crossbody forces.
bar P = 1 over 2 sum from b = 1 to F %delta_1b left lbrace sum from stack { u = 0 # odd } to N sum from v = 1 to Q left ( -1 right ) ^{{u + 3} over 2} X_bv^2 %omega_1 k(b,u,v) %omega_b^u right rbrace
Equation 4.11
Subscripts:
u =	Order of derivative.
v =	Motion variable.
b =	Index of body (current equation assumes body 1 is the body in question.
N =	Maximum order of derivative.
Q =	Maximum number of variables of motion.
F =	Maximum number of bodies.

Variables:
k(b, u, v) =	Force coefficient for derivative u, motion variable v (obtained through evaluation of the motion model), operating on body b.
ωb =	Body encounter frequency for body of index b.
ω1 =	Body encounter frequency for body of index 1 (the current body).
Xbv =	Amplitude of body motion, for body b, motion variable v.
# Application to Custom Motion Models
The force coefficients are calculated through direct evaluation of each equation of motion within the motion model. Because of this, the average power extracted is accurate for any motion model specified, including any custom motion models.
# Response Amplitude Operator (RAO)
Most of the outputs are presented in two formats: the absolute value, and a response amplitude operator (RAO). The RAO gives the relative output for the given input. This can be useful when comparing the performance of the body on a general basis, independent of the given seastate. However, calculation of an RAO is not consistent through the industry or even from one input to the next. Section 6 addresses this by describing the exact calculation method of the RAO for each output.
## RAO Calculation
The RAO calculation is divided into two sections: first the RAO normalization is derived; and then the actual method of RAO application is shown. This may be specific to each RAO.
### RAO Normalization
The response amplitude operator is calculated through dividing the power by the wave amplitude, calculated in the body coordinate system, using the body encounter spectrum. shows power as a generic term. This equation is applied the same to all power calculations for each force type.
RAO(P) = bar P over %zeta_0b
Equation 6.1
Variables:
b =	Index of the body specified.
P =	Average power extracted.
ζ0b =	Amplitude of the wave, in the body coordinate system.
### RAO Application
The RAO can be applied with simply multiplying by the wave amplitude.
bar P = RAO(P) %zeta_ob
Equation 6.2
Variables:
b =	Index of the body specified.
RAO(P) =	Response amplitude operator to convert from incident wave amplitude, in the body coordinate system, over to the average power extracted.
ζ0b =	Amplitude of the wave, in the body coordinate system.

Sometimes, it is more convenient to apply the RAO directly to the wave energy spectrum. There are two wave energy spectra to select from: the body encounter spectrum, and the global wave spectrum. Equation 6.3 shows application of the global wave spectrum. This includes application of an additional RAO to convert from the global wave spectrum to the body encounter spectrum. The output from this calculation is the spectral energy density of the average power extracted.
S(P) = left ( RAO left ( P right ) right )^2 cdot left [ RAO(S(%omega_G)) cdot S(%omega_G) right ]
Equation 6.3
Variables:
RAO(P) =	RAO to convert from body wave amplitude to average power extracted.
RAO(S(%omega_G)) = ~	RAO to convert from global wave spectrum to body encountered spectrum.
S(ωG) =	Global wave spectrum, spectral energy density.
## RAO Units
The units of the resulting RAO output can become very confusing, depending on how the RAO gets calculated. This section clarifies by clearly stating the units for each RAO.
For power results, the RAO has units of Watts per meter.
left [ RAO(P) right ]_units = W over m = {N-m over s} over m = N over s = kg m over s^3
Equation 6.4
Variables:
N =	Newtons (N).
W =	Watts (W).
m =	Meters (m).
s =	Seconds (s).
kg =	Kilograms (kg)..