6DOF Motion Model
# Introduction
The six degree of freedom (6DOF) motion model includes all six degrees of freedom for a rigid body. This is the most common model for dynamics solvers. Common applications include:
1. Vessels in a seaway
2. Small boats or objects stationary in a seaway
3. Buoy motions.

The 6DOF model includes the full level of detail. It is the most accurate of the standard motion models included in oFreq. However, because of this accuracy, it also requires the most data for accurate input values. Standard hydrodynamic coefficients from a robust radiation-diffraction solver should supply data for all six degrees of freedom. Additional information will be required, such as ship mass and mass moment of inertia.
If you do not have reliable data for all motions, consider using a more simplistic motion model. Remember that all equations interact with each other. Unreliable data in one equation could lead to large errors in other equations.
The 6DOF model has six equations and six variables. The variables are:
1. TX = x0: Translation in the X-axis (m).
2. TY = x1: Translation in the Y-axis (m).
3. TZ = x2: Translation in the Z-axis (m).
4. RX = x3: Rotation about the X-axis (rad).
5. RY = x4: Rotation about the Y-axis (rad).
6. RZ = x5: Rotation about the Z-axis (rad).
# General Equation Context
The 6DOF model involves repetition of a basic concept for six different equations. The following equations shows the generic concept equation.
Mass + Origin Offset Terms + ~ newline sum from derivative left ( sum from {motion variable} Hydrodynamic Reactive Forces right ) + ~ newline sum from derivative left ( sum from {motion variable} User Reactive Forces right ) + ~ newline sum from bodies left [ sum from derivative left ( sum from {motion variable} Hydrodynamic Crossbody Forces right ) right ] + ~ newline sum from bodies left [ sum from derivative left ( sum from {motion variable} User Crossbody Forces right ) right ] + ~ newline newline ~ = ~ newline newline Hydrodynamic Active Force + ~ newline User Active Force
Equation 2.1

# Translation X - Equation 1 (x1)
The translation x equation is the first of three translation motion equations. All terms are in the body coordinate system.
Pay careful attention to the subscript notations. These six equations will start to look very similar, and the only major difference between them is the subscript notation.
M {d^2 underline x1} over dt^2 + M z_g {d^2 underline x5} over dt^2 - M y_g {d^2 underline x6} over dt^2 + ~ newline sum from u = 0 to 2 left ( sum from v = 1 to 6 C(u)_{HydroReact(1,v)} {d^u underline x_v} over dt^u right ) + ~ newline sum from u = 0 to N left ( sum from v = 1 to 6 C(u)_{UserReact(1,v)} {d^u underline x_v} over dt^u right ) + ~ newline sum from b = 1 to F %delta_1b left [ sum from u = 0 to 2 left ( sum from v = 1 to 6 C(u,b)_{HydroCross(1,v)} {d^u underline x_v} over dt^u right ) right ] + ~ newline sum from b = 1 to F %delta_0b left [ sum from u = 0 to N left ( sum from v = 1 to 6 C(u,b)_{UserCross(1,v)} {d^u underline x_v} over dt^u right ) right ] + ~ newline newline ~ = ~ newline newline underline F1_HydroActive + ~ newline underline F1_UserActive
Equation 3.1
Subscripts:
v =	Variable index of x1 to x6 (1 to 6).
u =	Order of derivative (0 to 2 for hydrodynamic forces, 0 to N for user forces).
b =	Index of the body for a cross body force (1 to M).
N =	Highest order of derivative for user forces.
F =	Total number of bodies

Variables:
M =	Mass of body.
yg =	Y-axis distance from center of gravity to point of rotation.
zg =	Z-axis distance from center of gravity to point of rotation.
C(u)HydroReact(1,v) =	Hydrodynamic input coefficient for reaction forces for variable v of derivative u.
C(u)UserReact(1,v) =	User input coefficient for reaction forces for variable v of derivative u.
C(u,b)HydroCross(1,v) =	Hydrodynamic input coefficient for reaction forces for variable v of derivative u, linking to body b.
C(u,b)UserCross(1,v) =	User input coefficient for reaction forces for variable v of derivative u, linking to body b.
δ1b =	Kronecker Delta. Just a fancy math term that means when b = 1, the value is zero, and that part of the summation does not count.
F1HydroActive =	Hydrodynamic active force for body.
F1UserActive =	User defined active force for the body.

The underline notation means a complex number.

# Translation Y - Equation 2 (x2)
The translation y equation is the second of three translation motion equations. All terms are in the body coordinate system.
Pay careful attention to the subscript notations. These six equations will start to look very similar, and the only major difference between them is the subscript notation.
M {d^2 underline x2} over dt^2 - M z_g {d^2 underline x4} over dt^2 + M x_g {d^2 underline x6} over dt^2 + ~ newline sum from u = 0 to 2 left ( sum from v = 1 to 6 C(u)_{HydroReact(2,v)} {d^u underline x_v} over dt^u right ) + ~ newline sum from u = 0 to N left ( sum from v = 1 to 6 C(u)_{UserReact(2,v)} {d^u underline x_v} over dt^u right ) + ~ newline sum from b = 1 to F %delta_1b left [ sum from u = 0 to 2 left ( sum from v = 1 to 6 C(u,b)_{HydroCross(2,v)} {d^u underline x_v} over dt^u right ) right ] + ~ newline sum from b = 1 to F %delta_1b left [ sum from u = 0 to N left ( sum from v = 1 to 6 C(u,b)_{UserCross(2,v)} {d^u underline x_v} over dt^u right ) right ] + ~ newline newline ~ = ~ newline newline underline F2_HydroActive + ~ newline underline F2_UserActive
Equation 4.1
Variables:
M =	Mass of body.
xg =	X-axis distance from center of gravity to point of rotation.
zg =	Z-axis distance from center of gravity to point of rotation.
C(u)HydroReact(2,v) =	Hydrodynamic input coefficient for reaction forces for variable v of derivative u.
C(u)UserReact(2,v) =	User input coefficient for reaction forces for variable v of derivative u.
C(u,b)HydroCross(2,v) =	Hydrodynamic input coefficient for reaction forces for variable v of derivative u, linking to body b.
C(u,b)UserCross(2,v) =	User input coefficient for reaction forces for variable v of derivative u, linking to body b.
δ2b =	Kronecker Delta. Just a fancy math term that means when b = 2, the value is zero, and that part of the summation does not count.
F2HydroActive =	Hydrodynamic active force for body.
F2UserActive =	User defined active force for the body.

The underline notation means a complex number.
# Translation Z - Equation 3 (x3)
The translation z equation is the third of three translation motion equations. All terms are in the body coordinate system.
Pay careful attention to the subscript notations. These six equations will start to look very similar, and the only major difference between them is the subscript notation.
M {d^2 underline x3} over dt^2 + M y_g {d^2 underline x4} over dt^2 - M x_g {d^2 underline x5} over dt^2 + ~ newline sum from u = 0 to 2 left ( sum from v = 1 to 6 C(u)_{HydroReact(3,v)} {d^u underline x_v} over dt^u right ) + ~ newline sum from u = 0 to N left ( sum from v = 1 to 6 C(u)_{UserReact(3,v)} {d^u underline x_v} over dt^u right ) + ~ newline sum from b = 1 to F %delta_1b left [ sum from u = 0 to 2 left ( sum from v = 1 to 6 C(u,b)_{HydroCross(3,v)} {d^u underline x_v} over dt^u right ) right ] + ~ newline sum from b = 1 to F %delta_1b left [ sum from u = 0 to N left ( sum from v = 1 to 6 C(u,b)_{UserCross(3,v)} {d^u underline x_v} over dt^u right ) right ] + ~ newline newline ~ = ~ newline newline underline F3_HydroActive + ~ newline underline F3_UserActive
Equation 5.1
Variables:
M =	Mass of body.
xg =	X-axis distance from center of gravity to point of rotation.
yg =	Y-axis distance from center of gravity to point of rotation.
C(u)HydroReact(3,v) =	Hydrodynamic input coefficient for reaction forces for variable v of derivative u.
C(u)UserReact(3,v) =	User input coefficient for reaction forces for variable v of derivative u.
C(u,b)HydroCross(3,v) =	Hydrodynamic input coefficient for reaction forces for variable v of derivative u, linking to body b.
C(u,b)UserCross(3,v) =	User input coefficient for reaction forces for variable v of derivative u, linking to body b.
δ3b =	Kronecker Delta. Just a fancy math term that means when b = 3, the value is zero, and that part of the summation does not count.
F3HydroActive =	Hydrodynamic active force for body.
F3UserActive =	User defined active force for the body.

The underline notation means a complex number.
# Rotation X - Equation 4 (x4)
The rotation x equation is the first of three rotation motion equations. All terms are in the body coordinate system.
Pay careful attention to the subscript notations. These six equations will start to look very similar, and the only major difference between them is the subscript notation.
- M z_g {d^2 underline x2} over dt^2 + M y_g {d^2 underline x3} over dt^2 + I_xx {d^2 underline x4} over dt^2 - I_xy {d^2 underline x5} over dt^2 - I_xz {d^2 underline x6} over dt^2 ~ newline sum from u = 0 to 2 left ( sum from v = 1 to 6 C(u)_{HydroReact(4,v)} {d^u underline x_v} over dt^u right ) + ~ newline sum from u = 0 to N left ( sum from v = 1 to 6 C(u)_{UserReact(4,v)} {d^u underline x_v} over dt^u right ) + ~ newline sum from b = 1 to F %delta_1b left [ sum from u = 0 to 2 left ( sum from v = 1 to 6 C(u,b)_{HydroCross(4,v)} {d^u underline x_v} over dt^u right ) right ] + ~ newline sum from b = 1 to F %delta_1b left [ sum from u = 0 to N left ( sum from v = 1 to 6 C(u,b)_{UserCross(4,v)} {d^u underline x_v} over dt^u right ) right ] + ~ newline newline ~ = ~ newline newline underline F4_HydroActive + ~ newline underline F4_UserActive
Equation 6.1
Variables:
M =	Mass of body.
yg =	Y-axis distance from center of gravity to point of rotation.
zg =	Z-axis distance from center of gravity to point of rotation.
Ixx =	Mass moment of inertia in the X-axis.
Ixy =	Cross product of inertia in the X-Y-axis.
Ixz =	Cross product of inertia in the X-Z-axis.
C(u)HydroReact(4,v) =	Hydrodynamic input coefficient for reaction forces for variable v of derivative u.
C(u)UserReact(4,v) =	User input coefficient for reaction forces for variable v of derivative u.
C(u,b)HydroCross(4,v) =	Hydrodynamic input coefficient for reaction forces for variable v of derivative u, linking to body b.
C(u,b)UserCross(4,v) =	User input coefficient for reaction forces for variable v of derivative u, linking to body b.
δ4b =	Kronecker Delta. Just a fancy math term that means when b = 4, the value is zero, and that part of the summation does not count.
F4HydroActive =	Hydrodynamic active force for body.
F4UserActive =	User defined active force for the body.

The underline notation means a complex number.
# Rotation Y - Equation 5 (x5)
The rotation y equation is the second of three rotation motion equations. All terms are in the body coordinate system.
Pay careful attention to the subscript notations. These six equations will start to look very similar, and the only major difference between them is the subscript notation.
M z_g {d^2 underline x1} over dt^2 - M x_g {d^2 underline x3} over dt^2 - I_xy {d^2 underline x4} over dt^2 + I_yy {d^2 underline x5} over dt^2 - I_yz {d^2 underline x6} over dt^2 ~ newline sum from u = 0 to 2 left ( sum from v = 1 to 6 C(u)_{HydroReact(5,v)} {d^u underline x_v} over dt^u right ) + ~ newline sum from u = 0 to N left ( sum from v = 1 to 6 C(u)_{UserReact(5,v)} {d^u underline x_v} over dt^u right ) + ~ newline sum from b = 1 to F %delta_1b left [ sum from u = 0 to 2 left ( sum from v = 1 to 6 C(u,b)_{HydroCross(5,v)} {d^u underline x_v} over dt^u right ) right ] + ~ newline sum from b = 1 to F %delta_1b left [ sum from u = 0 to N left ( sum from v = 1 to 6 C(u,b)_{UserCross(5,v)} {d^u underline x_v} over dt^u right ) right ] + ~ newline newline ~ = ~ newline newline underline F5_HydroActive + ~ newline underline F5_UserActive
Equation 7.1
Variables:
M =	Mass of body.
yg =	Y-axis distance from center of gravity to point of rotation.
zg =	Z-axis distance from center of gravity to point of rotation.
Iyy =	Mass moment of inertia in the Y-axis.
Ixy =	Cross product of inertia in the X-Y-axis.
Iyz =	Cross product of inertia in the Y-Z-axis.
C(u)HydroReact(5,v) =	Hydrodynamic input coefficient for reaction forces for variable v of derivative u.
C(u)UserReact(5,v) =	User input coefficient for reaction forces for variable v of derivative u.
C(u,b)HydroCross(5,v) =	Hydrodynamic input coefficient for reaction forces for variable v of derivative u, linking to body b.
C(u,b)UserCross(5,v) =	User input coefficient for reaction forces for variable v of derivative u, linking to body b.
δ5b =	Kronecker Delta. Just a fancy math term that means when b = 5, the value is zero, and that part of the summation does not count.
F5HydroActive =	Hydrodynamic active force for body.
F5UserActive =	User defined active force for the body.

The underline notation means a complex number.
# Rotation Z - Equation 6 (x6)
The rotation z equation is the third of three rotation motion equations. All terms are in the body coordinate system.
Pay careful attention to the subscript notations. These six equations will start to look very similar, and the only major difference between them is the subscript notation.
- M y_g {d^2 underline x1} over dt^2 + M x_g {d^2 underline x2} over dt^2 - I_xz {d^2 underline x4} over dt^2 - I_yz {d^2 underline x5} over dt^2 + I_zz {d^2 underline x6} over dt^2 ~ newline sum from u = 0 to 2 left ( sum from v = 1 to 6 C(u)_{HydroReact(6,v)} {d^u underline x_v} over dt^u right ) + ~ newline sum from u = 0 to N left ( sum from v = 1 to 6 C(u)_{UserReact(6,v)} {d^u underline x_v} over dt^u right ) + ~ newline sum from b = 1 to F %delta_1b left [ sum from u = 0 to 2 left ( sum from v = 1 to 6 C(u,b)_{HydroCross(6,v)} {d^u underline x_v} over dt^u right ) right ] + ~ newline sum from b = 1 to F %delta_1b left [ sum from u = 0 to N left ( sum from v = 1 to 6 C(u,b)_{UserCross(6,v)} {d^u underline x_v} over dt^u right ) right ] + ~ newline newline ~ = ~ newline newline underline F6_HydroActive + ~ newline underline F6_UserActive
Equation 8.1
Variables:
M =	Mass of body.
xg =	X-axis distance from center of gravity to point of rotation.
yg =	Z-axis distance from center of gravity to point of rotation.
Izz =	Mass moment of inertia in the Y-axis.
Ixz =	Cross product of inertia in the X-Z-axis.
Iyz =	Cross product of inertia in the Y-Z-axis.
C(u)HydroReact(6,v) =	Hydrodynamic input coefficient for reaction forces for variable v of derivative u.
C(u)UserReact(6,v) =	User input coefficient for reaction forces for variable v of derivative u.
C(u,b)HydroCross(6,v) =	Hydrodynamic input coefficient for reaction forces for variable v of derivative u, linking to body b.
C(u,b)UserCross(6,v) =	User input coefficient for reaction forces for variable v of derivative u, linking to body b.
δ6b =	Kronecker Delta. Just a fancy math term that means when b = 6, the value is zero, and that part of the summation does not count.
F6HydroActive =	Hydrodynamic active force for body.
F6UserActive =	User defined active force for the body.

The underline notation means a complex number.