Wave Directions
# Result
The wave directions is a list of wave directions used in the analysis. This essentially repeats back the list of directions the user input for the analysis. The output provides two useful things:
1. The direction list confirms the inputs the user specified.
2. The direction list shows the sequence of wave directions used. This is important because oFreq will not list the wave direction in subsequent outputs. Other outputs are simply stored under folders. Each folder represents a single wave direction. Folders are just numbered in sequence. Folder “d1” corresponds to the first wave direction in the list; folder “d2” corresponds to the second direction in the list, and so on.
## Units of Measurement
Wave directions are measured in units of radians, positive counter-clockwise. All wave directions are measured in the global coordinate system. A direction of zero radians points to True North.
# Assumptions / Limitations
The output of wave directions makes the following simple assumptions.
At least one wave direction was entered for the analysis.
# Variable Dependencies
The list of wave directions does not depend on any other variable in the analysis. It is an independent variable.
# Derivation
No derivation is necessary. The list of wave directions is an input provided by the user.
# Application to Custom Motion Models
The list of wave directions does not depend on the motion model applied. This output remains valid for any motion model.
# Response Amplitude Operator (RAO)
Most of the outputs are presented in two formats: the absolute value, and a response amplitude operator (RAO). The RAO gives the relative output for the given input. This can be useful when comparing the performance of the body on a general basis, independent of the given seastate. However, calculation of an RAO is not consistent through the industry or even from one input to the next. Section 6 addresses this by describing the exact calculation method of the RAO for each output.
## RAO Calculation
The list of wave directions has no significance when calculated as an RAO. No RAO's are calculated for the list of wave directions.