Body Encounter Frequency
# Result
This provides the list of body encounter frequencies. These are the global wave frequencies, converted over to the encounter frequency based on body forward velocity and wave encounter angle.
1. Each folder for wave directions will include an output of body encounter frequency.
2. Each body will have its own set of encounter frequencies.
3. The sequence of encounter frequencies match the sequence of global wave frequencies. For more information, see the section on global wave frequencies.
## Units of Measurement
The body encounter frequencies are measured in radians per second (rad/s).
# Assumptions / Limitations
The output of body encounter frequencies makes the following simple assumptions.
At least one wave frequency was entered for the analysis.
The output does not depend on the body having a forward velocity. This output will still calculate if no forward velocity is defined. In that situation, the body encounter frequency will match the global wave frequency.
# Variable Dependencies
The body encounter frequency depends on the following inputs:
1. Body forward velocity
2. Body heading
3. Global wave heading
4. Global wave frequency
# Derivation
Equation 4.1 shows the formula to calculate the body encounter frequency from global wave frequency.
%omega_B = %omega_G - {%omega_G^2 U} over g cos (%alpha_B - %alpha_G)
Equation 4.1
Variables:
ωB =	Body encounter frequency.
ωG =	Global wave frequency.
U =	Body forward velocity.
g =	Acceleration due to gravity (9.8065 m/s).
αB =	Heading of the body, relative to true north.
αG =	Direction of travel for the global wave defined, relative to true north.
# Application to Custom Motion Models
The list of body encounter frequencies does not depend on the motion model selected. This output is always valid, regardless of the motion model.
# Response Amplitude Operator (RAO)
Most of the outputs are presented in two formats: the absolute value, and a response amplitude operator (RAO). The RAO gives the relative output for the given input. This can be useful when comparing the performance of the body on a general basis, independent of the given seastate. However, calculation of an RAO is not consistent through the industry or even from one input to the next. Section 6 addresses this by describing the exact calculation method of the RAO for each output.
## RAO Calculation
The RAO calculation is divided into two sections: first the RAO normalization is derived; and then the actual method of RAO application is shown. This may be specific to each RAO.
### RAO Normalization
The RAO is normalized by dividing by the global encounter frequency. (Equation 6.1)
RAO(%omega_B) = %omega_B over %omega_G = 1 - {%omega_G U} over g cos (%alpha_B - %alpha_G)
Equation 6.1
Variables:
ωB =	Body encounter frequency.
ωG =	Global wave frequency.
U =	Body forward velocity.
g =	Acceleration due to gravity (9.8065 m/s).
αB =	Heading of the body, relative to true north.
αG =	Direction of travel for the global wave defined, relative to true north.
### RAO Application
The RAO may be used to convert from global wave frequency to body encounter frequency by simple multiplication.
%omega_B = RAO(%omega_B) %omega_G
Equation 6.2
The RAO does depend on the input global wave frequency. Each RAO data point is only applicable to that specific input for global wave frequency. However, you can safely interpolate for other values of global wave frequency (linear interpolation will be accurate).
## RAO Units
The units of the resulting RAO output can become very confusing, depending on how the RAO gets calculated. This section clarifies by clearly stating the units for each RAO.
This RAO is dimensionless. (Equation 6.3)
[RAO(%omega_B)]_units = {rad/s} over {rad/s} = unitless
Equation 6.3