Wave Spectra
# Result
This output describes the applied wave spectra used in each wave direction. The applied wave spectra are described in terms of spectral energy density. This energy density varies with global wave frequency. The user defines the wave spectrum, but this definition is usually formula based. The wave spectrum may vary with wave direction and the user only entered simple formula coefficients. This output provides the exact spectral energy density for each wave frequency, and each wave direction.
## Units of Measurement
The spectral energy density has units of meters squared per radian per second.
m2/(rad/s)
# Assumptions / Limitations
The only limitation is that a spectral energy density applied to a single wave direction is not applicable to other wave directions. Each wave direction is defined as its own independent wave energy spectrum. Otherwise, the spectral energy density has no limitations. It is part of classic seakeeping theory.
# Variable Dependencies
The spectral energy density depends on the following variables
1. Global wave direction.
2. Global wave frequency.
# Derivation
The spectral energy density itself is an input, either supplied by the user, or derived from industry formula for idealized wave spectra. More important is the formula to convert from the spectral energy density to wave amplitude.
%zeta_0 = sqrt{2 S(%omega_G) ` %delta %omega_G}
Equation 4.1
Variables:
ζ0 =	Wave amplitude for the given global wave frequency.
S(ωG) =	Spectral energy density for the given global wave frequency.
δωG =	Change in wave frequency.

The spectral energy density is always defined in terms of the global wave frequency.
The change in wave frequency can be a tricky calculation. Normally, oFreq defines it as the average of the change in frequency above and below the frequency in question.
%delta %omega_Gi = {%omega_{Gi+1} + %omega_{Gi-1}} over 2
Equation 4.2
Variables:
i =	Index of the current wave frequency in question.
δωGi =	Change in wave frequency for the wave frequency i.
ωGi+1 =	Wave frequency at index (i+1). That is one frequency higher than the current frequency.
ωGi-1 =	Wave frequency at index (i-1). That is one frequency lower than the current frequency.

However, this definition does not work for the first wave frequency (ω1) and the last wave frequency (ωN). Special definitions must be used for these cases.
For the first wave frequency (ω1), the change in wave frequency is defined by Equation 4.3
%delta %omega_G1 = %omega_G2 - %omega_G1
Equation 4.3
Variables:
δωG1 =	Change in wave frequency for the first wave frequency.
ωG2 =	Wave frequency at index 2. That is one frequency higher than the current frequency.
ωG1 =	Wave frequency at index 1. That is the current wave frequency.

For the last wave frequency (ωN), the change in wave frequency is defined by Equation 4.4
%delta %omega_GN = %omega_GN - %omega_{G `N-1}
Equation 4.4
Variables:
δωGN =	Change in wave frequency for the last wave frequency (index N).
ωGN =	Wave frequency at index N. That is the last wave frequency.
ωGN-1 =	Wave frequency at index N-1. That is one lower than the current wave frequency.
# Application to Custom Motion Models
This output is independent of the motion model applied. It is valid for any motion model.
# Response Amplitude Operator (RAO)
Most of the outputs are presented in two formats: the absolute value, and a response amplitude operator (RAO). The RAO gives the relative output for the given input. This can be useful when comparing the performance of the body on a general basis, independent of the given seastate. However, calculation of an RAO is not consistent through the industry or even from one input to the next. Section 6 addresses this by describing the exact calculation method of the RAO for each output.
## RAO Calculation
The RAO calculation is divided into two sections: first the RAO normalization is derived; and then the actual method of RAO application is shown. This may be specific to each RAO.
### RAO Normalization
The important part for a wave spectrum is to convert from the global wave frequencies to the body encounter frequencies. Thus, the RAO does not exactly present a normalization of the wave energy spectrum. Instead, it provides a conversion factor to calculate the wave energy spectrum encountered by the body, with forward velocity. (Equation 6.1)
RAO(S(%omega_G)) = {d %omega_G} over {d %omega_b} = g over {g - 2 %omega_G U cos (%alpha_b - %alpha_G)}
Equation 6.1
Variables:
U =	Body forward velocity.
g =	Acceleration due to gravity (9.8065 m/s).
ωG =	Global wave frequency.
αB =	Heading of the body, relative to true north.
αG =	Direction of travel for the global wave defined, relative to true north.
### RAO Application
The RAO can be applied by multiplying with the wave spectrum that was based on the global wave frequency. Note that once you use the RAO to convert from global wave spectrum to body encounter spectrum, the body encounter spectrum should be compared against the body encounter frequencies, not against the global wave frequencies.
S(%omega_b) = RAO(S(%omega_G)) cdot S(%omega_G)
Equation 6.2
Variables:
RAO(S(ωG)) =	Response amplitude operator (RAO) for the body in question.
S(ωG) =	Wave spectrum, based on global wave frequency.
S(ωB) =	Wave spectrum, based on body encounter frequency for the body in question.
## RAO Units
The units of the resulting RAO output can become very confusing, depending on how the RAO gets calculated. This section clarifies by clearly stating the units for each RAO.
The RAO for the energy spectrum is unitless.
left [ RAO(S(%omega_G)) right ]_units = (rad/s) over (rad/s) = unitless
Equation 6.3