Body Forces
# Result
This output calculates the force resulting from each of the reactive body forces. The output is given as a complex number. The complex number indicates both the magnitude of the force, and its relative phase angle to the incident waves. The actual value of the force is only the real component of the values reported in this output. The imaginary component is only included to derive the phase angle of the force response.
Here force is a generic term and can mean either a translation force or a rotation moment, depending on the equation of motion.
oFreq reports the results for the active forces and the reactive forces. The active forces are important for checking inputs and the results of any interpolation on the hydrodynamic side. Although, most of the calculation efforts goes into the reactive forces.
oFreq will report a result for every reactive force defined in the analysis. This includes hydrodynamic forces automatically defined by inclusion of a hydrodynamic body. The reactive force from body mass is also included in the output. oFreq considers each force definition to be its own object. Output information is organized with the same structure that the forces were defined in the analysis.
When oFreq calculates the result of the reactive force, it evaluates all derivatives of a force and substitutes the values of all variables that the force depended on. This creates a combined result that accounts for all influences defined within that force object.
When defining the force objects in oFreq, consider what level of detail you want when oFreq reports the outputs. For example, if you want to separate out the influence of individual variables within a single physical force, you must define it as two separate force objects in oFreq. That way oFreq can evaluate the influence separately.
The one catch to the direct evaluation method is that oFreq only calculates the resultant force for each individual equation defined within a force object. For example, if a reactive force included influences from equations for x1, x2, and x3, then oFreq would report three component results for that force, one for each equation. This limitation is necessary because, although oFreq knows the relationship between different equations of motion, it can not know the physically correct way to combine results from equations.
## Units of Measurement
The units of output depend on the equation of motion for each component of the force. Generally, the force components can only be defined as a translation force or a rotation moment. This will result in the following units of measurement.
1. Translation force: units of Newtons (N).
2. Rotation moment: units of Newton-meters (N-m).
# Assumptions / Limitations
oFreq only calculates the resultant force for each individual equation defined within a force object. For example, if a reactive force included influences from equations for x1, x2, and x3, then oFreq would report three component results for that force, one for each equation. This limitation is necessary because, although oFreq knows the relationship between different equations of motion, it can not know the physically correct way to combine results from equations.
# Variable Dependencies
The resultant forces depend on the following elements.
1. The body selected.
2. Global wave frequency.
3. Global wave spectrum.
4. Global wave direction.
5. Body heading.
6. Influences of all reactive and active forces.
7. The motion model selected.
# Derivation
The motion model calculates the force through substitution of its input coefficients and substitution of the solved variables of motion. These numbers are all substituted into the equation of motion. Then the equation of motion is directly evaluated to find the resultant force. The motion model resets, and this process repeats for each equation of motion and each reactive force defined.
The exact computation changes slightly depending on which type of force is evaluated. The following equations show the equivalent summation for each force type.
## User Reactive Force
underline {F(w)_UserReact} = sum from u = 0 to N left ( sum from v = 1 to Q C(u,v)_UserReact {d^u underline x_v} over {dt^u} right )
Equation 4.1
Subscripts:
w =	Equation index.
u =	Order of derivative.
v =	Variable of motion.
N =	Highest order of derivative.
Q =	Total number of motion variables.
Variables:
C(u,v)UserReact =	User input for reaction force on variable v for derivative u.
xv =	Motion variable v.
Underline notation denotes a complex variable.
## Hydrodynamic Reactive Force
underline {F(w)_HydroReact} = sum from u = 0 to 2 left ( sum from v = 1 to 6 C(u,v)_HydroReact {d^u underline x_v} over {dt^u} right )
Equation 4.2
Subscripts:
w =	Equation index.
u =	Order of derivative.
v =	Variable of motion.

Variables:
C(u,v)HydroReact =	Hydrodynamic input for reaction force on variable v for derivative u.
xv =	Motion variable v.
Underline notation denotes a complex variable.
## Mass Force
underline {F(w)_Mass} = sum from u = 0 to 2 left ( sum from v = 1 to 6 C(u,v)_HydroReact {d^u underline x_v} over {dt^u} right )
Equation 4.3
Subscripts:
w =	Equation index.
u =	Order of derivative.
v =	Variable of motion.

Variables:
C(u,v)HydroReact =	Hydrodynamic input for reaction force on variable v for derivative u.
xv =	Motion variable v.
Underline notation denotes a complex variable.
## User Crossbody Force
Note that Equation 4.4 assumes the calculation is for resultant force received on body 1. The value of the Kronecker delta changes when the forces are calculated for other receiving bodies.
underline {F(w)_UserCross} = sum from b = 1 to M %delta_1b left [sum from u = 0 to N left ( sum from v = 1 to Q C(u,v,b)_UserCross {d^u underline x_vb} over {dt^u} right ) right ]
Equation 4.4
Subscripts:
w =	Equation index.
u =	Order of derivative.
v =	Variable of motion.
b =	Index of bodies.
M =	Total number of bodies
N =	Highest order of derivative.
Q =	Total number of motion variables.

Variables:
C(u,v,b)UserCross =	User input for reaction force on variable v for derivative u, using body b as the sending body.
xv =	Motion variable v, using body b as the sending body.
δ1b =	Anti Kronecker delta. Returns positive when b does not equal 1.
Underline notation denotes a complex variable.
## Hydrodynamic Crossbody Force
Note that Equation 4.5 assumes the calculation is for resultant force received on body 1. The value of the Kronecker delta changes when the forces are calculated for other receiving bodies.
underline {F(w)_HydroCross} = sum from b = 1 to M %delta_1b left [sum from u = 0 to 2 left ( sum from v = 1 to 6 C(u,v,b)_HydroCross {d^u underline x_vb} over {dt^u} right ) right ]
Equation 4.5
Subscripts:
w =	Equation index.
u =	Order of derivative.
v =	Variable of motion.
b =	Index of bodies.
M =	Total number of bodies

Variables:
C(u,v,b)HydroCross =	User input for reaction force on variable v for derivative u, using body b as the sending body.
xv =	Motion variable v, using body b as the sending body.
δ1b =	Anti Kronecker delta. Returns positive when b does not equal 1.
Underline notation denotes a complex variable.
## User Active Force
underline {F(w)_UserActive} = underline {C_UserActive}
Equation 4.6
Subscripts:
w =	Equation index.

Variables:
CUserActive =	User input coefficient for active force.
Underline notation denotes a complex variable.
## Hydrodynamic Active Force
underline {F(w)_HydroActive} = underline {C_HydroActive}
Equation 4.7
Subscripts:
w =	Equation index.

Variables:
CHydroActive =	User input coefficient for active force.
Underline notation denotes a complex variable.
# Application to Custom Motion Models
The forces are calculated through direct evaluation of each equation of motion within the motion model. Because of this, the calculated forces are accurate for any motion model specified, including any custom motion models.
# Response Amplitude Operator (RAO)
Most of the outputs are presented in two formats: the absolute value, and a response amplitude operator (RAO). The RAO gives the relative output for the given input. This can be useful when comparing the performance of the body on a general basis, independent of the given seastate. However, calculation of an RAO is not consistent through the industry or even from one input to the next. Section 6 addresses this by describing the exact calculation method of the RAO for each output.
## RAO Calculation
The RAO calculation is divided into two sections: first the RAO normalization is derived; and then the actual method of RAO application is shown. This may be specific to each RAO.
### RAO Normalization
The response amplitude operator is calculated through dividing the force by the wave amplitude, calculated in the body coordinate system, using the body encounter spectrum. Equation 6.1 shows force as a generic term. This equation is applied the same to all force types.
The original forces were a complex variable, which tracked the magnitude of the response and it phase angle relative to the incident wave. However, RAO's are often used to quickly generalize a set of results and apply them to another situation. In that case, the phase angle of the force might not be accurate to the next situation. So only the magnitude of the RAO is reported. This provided a worst case scenario.
In reality, the difference in phase angles mean that the maximum motions never occur at that same time. The real force will always be less than the magnitude reported through the RAO. But the exact quantity can not be accurately reported through application of an RAO. The conservative approach was to only report the magnitude.
RAO(F) = left ldline underline {F} over %zeta_0b right rdline
Equation 6.1
Variables:
b =	Index of the body specified.
F =	Generic output force
ζ0b =	Amplitude of the wave, in the body coordinate system.
Underline notation denotes a complex number.
### RAO Application
The RAO can be applied with simply multiplying by the wave amplitude.
F = RAO(F) %zeta_ob
Equation 6.2
Variables:
b =	Index of the body specified.
RAO(F) =	Response amplitude operator for the force.
ζ0b =	Amplitude of the wave, in the body coordinate system.

Sometimes, it is more convenient to apply the RAO directly to the wave energy spectrum. There are two wave energy spectra to select from: the body encounter spectrum, and the global wave spectrum. Equation 6.3 shows application of the global wave spectrum. This includes application of an additional RAO to convert from the global wave spectrum to the body encounter spectrum. The output from this calculation is the spectral energy density of the body force.
S(F) = left ( RAO left ( F right ) right )^2 cdot left [ RAO(S(%omega_G)) cdot S(%omega_G) right ]
Equation 6.3
Variables:
RAO(F) =	RAO to convert from body wave amplitude to body force.
RAO(S(%omega_G)) = ~	RAO to convert from global wave spectrum to body encountered spectrum.
S(ωG) =	Global wave spectrum, spectral energy density.
## RAO Units
The units of the resulting RAO output can become very confusing, depending on how the RAO gets calculated. This section clarifies by clearly stating the units for each RAO.
For force results, the units of the RAO change, depending on whether the RAO normalized a translation force or a rotation moment. Equation 6.4 shows the units for the RAO when normalizing a translation force.
left [ RAO(F) right ]_units = N over m = kg over s^2
Equation 6.4
Variables:
N =	Newtons (N)
m =	Meters (m)
kg =	Kilograms (kg)
s =	Seconds (s)

Equation 6.4 shows the units for the RAO when normalizing a rotation moment.
left [ RAO(F) right ]_units = {N-m} over m = N over m = kg {m over s^2}
Equation 6.5
Variables:
N =	Newtons (N)
m =	Meters (m)
kg =	Kilograms (kg)
s =	Seconds (s)