Local Acceleration
# Result
This output provides the components of a solution at a local point on the ship, converted into translation components. The body solution may include elements of both translation and rotation within its equations of motion. Due to differences in phase angles, these elements combine in complex ways to form different resultant motions at local points on the ship. This output combines the rotation and translation components to resolve a single motion, composed of only three translation components at some user defined position.
When oFreq calculates the output, it accounts for relative phase angles between all the body motions. The phase angles for body motions change depending on body encounter frequency. Because of this, the local solution is a linear function with respect to its physical position on the body, but non-linear with body encounter frequency.
First, oFreq calculates the local motion at the point specified, and then it calculates the acceleration of the solution at that point.
## Units of Measurement
The units of measurement are meters per second squared (m/s2).
units = m / s^2
Equation 1.1
Variables:
m =	Units of meters (m).
s =	Units of seconds (s).
# Assumptions / Limitations
This output makes the following assumptions.
1. This outputs assumes rigid body motion.
2. This output assumes an oscillatory motion at a steady state value. Transient effects are ignored.
3. This output assumes a standard six degree of freedom motion model (6DOF). The output will still calculate if not all of the 6DOF variables are included, but that will affect the final solution. And the output can not consider any motion variables that extend beyond rigid body motion (the reserved variables of 1 – 6).
4. Body motions are defined from the origin of the body coordinate system.
5. The coordinates of the local point of output are known and resolved within the body coordinate system.
# Variable Dependencies
This output depends on the following variables.
1. Body encounter frequency.
2. Global wave direction.
3. Body heading.
4. All the body input forces
5. Global wave spectrum
6. Position specified for the local solution.
# Derivation
## Local Motion Calculation
The body motion variables are first converted into the local motion variables. Equation 4.1 resolves local translation on the X-axis, in the body coordinate system. Equation 4.2 resolves local translation on the Y-axis, in the body coordinate system. Equation 4.3 resolves local translation on the Z-axis, in the body coordinate system. All equations assume the solution for the body motion variables is known.
underline s_1 = underline x_1 - r_by underline x_6 + r_bz underline x_5
Equation 4.1
Variables:
s1 =	Local translation motion on the X-axis, in the body coordinate system.
x1 =	Body motion variable, translation on the X-axis, in the body coordinate system.
x6 =	Body motion variable, rotation about the Z-axis, in the body coordinate system.
x5 =	Body motion variable, rotation about the Y-axis, in the body coordinate system.
rby =	Position of the local solution point, Y-axis coordinate.
rbz =	Position of the local solution point, Z-axis coordinate.
underline notation denotes a complex number.

underline s_2 = underline x_2 - r_bz underline x_4 + r_bx underline x_6
Equation 4.2
Variables:
s2 =	Local translation motion on the Y-axis, in the body coordinate system.
x2 =	Body motion variable, translation on the Y-axis, in the body coordinate system.
x4 =	Body motion variable, rotation about the X-axis, in the body coordinate system.
x6 =	Body motion variable, rotation about the Z-axis, in the body coordinate system.
rbx =	Position of the local solution point, X-axis coordinate.
rbz =	Position of the local solution point, Z-axis coordinate.
underline notation denotes a complex number.

underline s_3 = underline x_3 + r_by underline x_4 + r_bx underline x_5
Equation 4.3
Variables:
s3 =	Local translation motion on the Z-axis, in the body coordinate system.
x3 =	Body motion variable, translation on the Z-axis, in the body coordinate system.
x4 =	Body motion variable, rotation about the X-axis, in the body coordinate system.
x5 =	Body motion variable, rotation about the Y-axis, in the body coordinate system.
rbx =	Position of the local solution point, X-axis coordinate.
rby =	Position of the local solution point, Y-axis coordinate.
underline notation denotes a complex number.
## Derivations Based on Local Motion
All body motion variables are oscillatory motion of the form shown in Equation 4.4. And all local solutions are linear combinations of the body motion variables. Consequently, the local solution will also be of the form shown in Equation 4.4. Thus, any order of derivative can be obtained from direct calculation of the derivative of the local solution.
underline x = underline X e^(j %omega_b t)
Equation 4.4
Variables:
x =	Some generic body motion variable.
X =	Amplitude of body motion variable.
j =	Imaginary number.
t =	Time.
ωb =	Body encounter frequency.
Underline notation denotes complex variable.

Equation 4.5 shows the calculation of acceleration of the local solution. The equation is applied the same wave to any of the three components of the local solution. This equation assumes the local solution variables are already solved.
{d^2 underline S_v} over {d t^2} = left ( j %omega_b right )^2 underline S_v
Equation 4.5
Variables:
v =	Index of the local solution variable in question (numbered 1 - 3).
Sv =	Amplitude of local solution variable, index v.
j =	Imaginary number.
ωb =	Body encounter frequency.
Underline notation denotes a complex variable.

The calculation of acceleration for the local solution depends on the body encounter frequency, and not the global wave frequency.
Although acceleration of the local solution is calculated based on body encounter frequency, it can still be compared to the global wave frequency. The dependency is a valid comparison.
But do not extend this concept to the response amplitude operators. The calculation of the RAO depends on the exact encountered wave spectrum and can not be generalized to the global wave frequency.
# Application to Custom Motion Models
This output assumes a standard six degree of freedom motion model (6DOF). The output will still calculate if not all of the 6DOF variables are included, but that will affect the final solution. And the output can not consider any motion variables that extend beyond rigid body motion (the reserved variables of 1 – 6).
This output will still work with custom motion models, but it can only access information for motion variables 1 – 6. These outputs are reserved for rigid body motions. If you require local solution information that includes the effects of other custom motion variables, this output will not return an accurate solution. Consider developing a custom output.
# Response Amplitude Operator (RAO)
Most of the outputs are presented in two formats: the absolute value, and a response amplitude operator (RAO). The RAO gives the relative output for the given input. This can be useful when comparing the performance of the body on a general basis, independent of the given seastate. However, calculation of an RAO is not consistent through the industry or even from one input to the next. Section 6 addresses this by describing the exact calculation method of the RAO for each output.
## RAO Calculation
The RAO calculation is divided into two sections: first the RAO normalization is derived; and then the actual method of RAO application is shown. This may be specific to each RAO.
### RAO Normalization
For all local solution variables, the RAO is normalized based on wave amplitude for the given body encounter spectrum. (Equation 6.1)
The original local solution variables were a complex variable, which tracked the magnitude of the response and it phase angle relative to the incident wave. However, RAO's are often used to quickly generalize a set of results and apply them to another situation. In that case, the phase angle of the force might not be accurate to the next situation. So only the magnitude of the RAO is reported. This provided a worst case scenario.
In reality, the difference in phase angles mean that the maximum motions never occur at that same time. The real motion will always be less than the magnitude reported through the RAO. But the exact quantity can not be accurately reported through application of an RAO. The conservative approach was to only report the magnitude.
RAO left ( {d^2 S_v} over {d t^2} right ) = left ldline left ({d^2 underline S_v} over {d t^2} right ) over %zeta_0b right ldline
Equation 6.1
Variables:
left ( {d^2 underline S_v} over {d t^2} right ) = ~	Acceleration of the local solution variable for the body for component v.
ζ0b =	Encountered wave amplitude for the body of index b.
v =	Index of the local motion component requested (1 – 3).
b =	Index of body specified.
Underline notation denotes a complex variable.

### RAO Application
The RAO can be applied with simply multiplying by the wave amplitude.
left ({d^2 S_v} over {d t^2} right ) = RAO left ( {d^2 S_v} over {d t^2} right ) ` %zeta_0b
Equation 6.2
Variables:
ζ0b =	Encountered wave amplitude for the body of index b.
v =	Index of the local motion component requested (1 – 3).
b =	Index of body specified.
RAO left ( {d^2 S_v} over {d t^2} right ) = ~	Response amplitude operator (RAO) to convert from body wave amplitude to local motion derivative, for component v.

Sometimes, it is more convenient to apply the RAO directly to the wave energy spectrum. There are two wave energy spectra to select from: the body encounter spectrum, and the global wave spectrum. Equation 6.3 shows application of the global wave spectrum. This includes application of an additional RAO to convert from the global wave spectrum to the body encounter spectrum. The output from this calculation is the spectral energy density for the acceleration of the local solution.
S left ({d^2 S_v} over {d t^2} right ) = left ( RAO left ( {d^2 S_v} over {d t^2} right ) right )^2 cdot left [ RAO(S(%omega_G)) cdot S(%omega_G) right ]
Equation 6.3
Variables:
RAO left ( {d^2 S_v} over {d t^2} right ) = ~	Response amplitude operator (RAO) to convert from body wave amplitude to local motion derivative, for component v.
RAO(S(%omega_G)) = ~	RAO to convert from global wave spectrum to body encountered spectrum.
S(ωG) =	Global wave spectrum, spectral energy density.
## RAO Units
The units of the resulting RAO output can become very confusing, depending on how the RAO gets calculated. This section clarifies by clearly stating the units for each RAO.
The units for acceleration of the local solution are s-2. (Equation 6.4)
left [ RAO left ( {d^2 S_v} over {d t^2} right ) right ]_units = m over {m s^2} = 1 over s^2 = s^-2
Equation 6.4
Variables:
m =	Units of meters (m).
s =	Units of seconds (s).