Outputs
# Calculation of Response Amplitude Operator
All outputs include the absolute magnitude of response. And the response amplitude operator (RAO) for that output. RAO's are their own list, given separately after the absolute response.
# Basic Feedback Outputs
These outputs essentially repeat the input the user set to create the analysis. They can be used to confirm the inputs set by the user. Also, some of the user inputs are just coefficients for industry formulas. These outputs show the computed results of those formulas.
## Wave_directions
\subpage wave_directions
## Wave Frequencies
\subpage wave_frequencies
## Body Encounter Frequencies
\subpage body_encounter_frequencies
## Output Wave Spectra
\subpage output_wave_spectra
# Body Solution Outputs
These outputs refer directly to the motion variables solved by oFreq. They relate to the motion variables encoded in each motion model. All other body outputs derive from these in some way. The outputs include the solution to the body motions and several critical derivatives of those outputs.
## Body Derivative
\subpage global_derivative
## Body Motion
\subpage global_motion
## Body Velocity
\subpage global_velocity
## Body Acceleration
\subpage global_acceleration
# Local Solution Outputs
The local solution outputs are derived from the body outputs. They coordinate the influences of the various body motions to determine the resultant local motions at user specified locations.
## Local Derivative
\subpage local_derivative
## Local Motion
\subpage local_motion
## Local Velocity
\subpage local_velocity
## Local Acceleration
\subpage local_acceleration
The output of the local acceleration does not include the effects of static gravity. This is because the outputs from oFreq are often used in statistical analysis and static gravity is a deterministic variable. Incorporating it into the other variables would confuse the results and invalidate any resultant statistical analysis.
## Local Dynamic Freeboard
\subpage local_dynamic_freeboard
# Force Outputs
Here force is a generic term that means both translation forces and rotation moments.
## Body Forces
\subpage global_force
# Power Outputs
Outputs about power are often used for research into items such as wave energy extraction devices. They may also be useful for preliminary assessments of body structures.
## Power
\subpage power
P_avg(%omega) = Re left lbrace left ( 1 over 2 + i over 2 right ) sum from j = 1 to n bar X _j^2 left [ sum from v = 0 to p k_jv (i)^{v+1} (%omega)^{v+1} right ] right rbrace
Equation 6.1
Variables:
Pavg(ω) =	Power produced, average over a single wave cycle.
i =	Imaginary number
j =	Summation index for motion variables that forces depend on.
v =	Summation index for derivatives included in each force.
n =	Total number of variables
p =	Highest order of derivative for forces
Xj =	Complex number for solution of variable motions.
kjv =	Force coefficient associated with each force number and derivative.
ω =	Wave frequency (rad/s)

# Efficiency Outputs
These are some customized outputs used by ofreq for efficiency assessments of wave energy extraction devices.
## Absolute Efficiency
\subpage efficiency_absolute
## Relative Efficiency
\subpage efficiency_relative
# Human Tolerance Outputs
Sometimes, human tolerances are the limiting criteria for seakeeping performance. oFreq includes outputs for classic algorithms on human tolerance, based on the ship motions.
## Local Motion Sickness Index
\subpage local_msi
## Local Subjective Motion Assessment
\subpage local_sma
# Custom Output Calculation
Because oFreq allows the user to define custom motion models, it is very easy to create systems of equations that exceed the capabilities of standard output calculations. Because of this, oFreq allows the user to define custom output calculations, similar to the definition of custom motion models.
\subpage custom_outputs