Body Coordinate System
Each body also has a local coordinate system.
1. For multiple-bodies, each body has its own coordinate system, independent of the other bodies.
2. This local coordinate system reorients with the body heading. All references to items on a body use
3. All body specific outputs are always written in the body coordinate system.
# Relating Global to Body Coordinates
The body coordinate system is first moved relative to the global coordinate system and then rotated with the body heading.
1. Translation of the body coordinate system happens first. Translation is specified by the position parameter. Coordinates of the body position are specified with the global coordinate system definition.
  1. X-axis is horizontal to the water surface, positive towards True North on the compass rose.
  2. Y-axis is horizontal to the water surface, positive towards True West on the compass rose.
  3. Z-axis is positive vertically up, out of the water.
2. Next the body is rotated by the heading specified.
  1. Rotation is about the origin defined by the position of the body coordinate system.
  2. Heading rotation is measured in units of radians [units].
  3. A heading of 0 rad points directly to True North.
  4. Heading rotates positive counter-clockwise.
# Origin
The origin can be defined wherever you want on the body. You can also insert comments in your input files to describe the origin location. The position input property is used to define the location of the body coordinate system, relative to the global origin.
# Translation Coordinates
All translation coordinates are relative to the origin defined for the body coordinates.
1. X-axis is horizontal to the water surface, positive direction depends on body heading.
2. Y-axis is horizontal to the water surface, positive direction depends on body heading.
3. Z-axis is positive vertically up, out of the water.

All translation coordinates are measured in units of meters. See the page on [units].
# Rotation Coordinates
All rotation coordinates are relative to the body coordinate system. All rotation coordinates follow the right hand rule.
1. Rotation about X-axis is positive rotating from the positive Y-axis to the positive Z-axis.
2. Rotation about Y-axis is positive rotating from the positive Z-axis to the positive X-axis.
3. Rotation about Z-axis is positive rotating from the positive X-axis to the positive Y-axis.
Rotation about the Z-axis does not change the body heading.
# Heading Coordinates
Heading measures angle of direction on the water surface, relative to the compass rose. Heading is treated just like rotation about the Z-axis.
1. Heading rotation is measured in units of radians [units].
2. A heading of 0 rad points directly to True North.
3. Heading rotates positive __counter-clockwise__.
4. This means that increasing heading goes from True North to True West.
  1. True North = heading of 0 rad.
  2. West = heading of π/2 (1.57 rad).
  3. South = heading of π (3.14 rad).
  4. East = heading of 3π /2 (4.71 rad).
# Coordinate System Transform
The following equations are used to convert from local body coordinates to global body coordinates.
x_G = x cos left ( - %alpha right ) + y sin left ( - %alpha right ) + P_x
Equation 6.1
y_G = -x sin left ( -%alpha right ) + y cos left ( - %alpha right ) + P_y
Equation 6.2
z_G = z + P_z
Equation 6.3
Variables:
xG =	X-axis coordinate, global coordinate system
-yG =	Y-axis coordinate, global coordinate system
zG =	Z-axis coordinate, global coordinate system
x =	X-axis coordinate, body coordinate system
y =	Y-axis coordinate, body coordinate system
z =	Z-axis coordinate, body coordinate system
Px =	Position to body, X-axis coordinate
Py =	Position to body, Y-axis coordinate
Pz =	Position to body, Z-axis coordinate
α =	Heading of body, relative to global coordinate system.

This transform can be considered as a transformation matrix.
left [ stack { x # y # z } right ] = left [ T right ] left [ stack { x_G # y_G # z_G } right ] + left [ P right ]
Equation 6.4
And the matrix [T] is defined as follows.
left [ T right ] = left [ matrix { cos(%alpha) # sin(%alpha) # 0 ## -sin(%alpha) # cos(%alpha) # 0 ## 0 # 0 # 1 } right ]
Equation 6.5
The matrix [T] is orthogonal. So the inverse is also the transpose of the matrix.
left [ T right ]^-1 = left [ T right ]^T = left [ matrix { cos(%alpha) # -sin(%alpha) # 0 ## sin(%alpha) # cos(%alpha) # 0 ## 0 # 0 # 1 } right ]
Equation 6.6
And the matrix [P] is defined as follows.
left [ P right ] = left [ stack { P_x # P_y # P_z } right ]
Equation 6.7

The combination of these matrices can be used to convert between global and body coordinate systems.
## Convert from Global to Body Coordinates
To convert from global to body coordinates, oFreq applies the following formula.
left [ stack { x # y # z } right ] = left [ T right ] left [ stack { x_G # y_G # z_G } right ] + left [ P right ] = left [ matrix { cos(%alpha) # sin(%alpha) # 0 ## -sin(%alpha) # cos(%alpha) # 0 ## 0 # 0 # 1 } right ] left [ stack { x_G # y_G # z_G } right ] + left [ stack { P_x # P_y # P_z } right ]
Equation 6.8
Variables:
[T] =	Coordinate axes transform matrix.
[P] =	Coordinate axes offset matrix.
xG =	X-axis coordinate, global coordinate system.
-yG =	Y-axis coordinate, global coordinate system.
zG =	Z-axis coordinate, global coordinate system.
x =	X-axis coordinate, body coordinate system.
y =	Y-axis coordinate, body coordinate system.
z =	Z-axis coordinate, body coordinate system.
Px =	Position to body, X-axis coordinate.
Py =	Position to body, Y-axis coordinate.
Pz =	Position to body, Z-axis coordinate.
α =	Heading of body, relative to global coordinate system.
## Convert from Body to Global Coordinates
To convert from body to global coordinates, oFreq applies the following formula.
left [ stack { x_G # y_G # z_G } right ] = left [ T right ]^T left [ stack { x # y # z } right ] - left [ P right ] = left [ matrix { cos(%alpha) # -sin(%alpha) # 0 ## sin(%alpha) # cos(%alpha) # 0 ## 0 # 0 # 1 } right ] left [ stack { x # y # z } right ] - left [ stack { P_x # P_y # P_z } right ]
Equation 6.9
Variables:
[T] =	Coordinate axes transform matrix.
[P] =	Coordinate axes offset matrix.
xG =	X-axis coordinate, global coordinate system.
-yG =	Y-axis coordinate, global coordinate system.
zG =	Z-axis coordinate, global coordinate system.
x =	X-axis coordinate, body coordinate system.
y =	Y-axis coordinate, body coordinate system.
z =	Z-axis coordinate, body coordinate system.
Px =	Position to body, X-axis coordinate.
Py =	Position to body, Y-axis coordinate.
Pz =	Position to body, Z-axis coordinate.
α =	Heading of body, relative to global coordinate system.