Body Motions
oFreq can solve for any set of vessel motions. Each vessel motion is called a degree of freedom (DOF) and assigned a variable that oFreq must solve. Within the documentation, these motions are numbered increasing, starting from 1. There is no programming limit on the number of variables to solve for. (Memory limitations of computer hardware ultimately limit number of variables.) However, the first six variables are reserved for rigid body motions. This is because oFreq also includes hydrodynamic effects and must know which variables to assign each hydrodynamic coefficient to.
# Standard Six Degree of Freedom Motions
The following definitions apply to vessel motions, assuming a rigid body, six degree of freedom motion.
Figure 1.1: Body Motions

Table 1.1: Body Motion Definitions (6 Degree of Freedom Model)
Index	Symbol	Motion Type	Vessel Motions	Positive Direction
1	x1	Translation	Surge	Positive along positive X-axis
2	x2	Translation	Sway	Positive along positive Y-axis
3	x3	Translation	Heave	Positive along positive Z-axis
4	x4	Rotation	Roll	Positive rotation about positive X-axis, following right hand rule.
5	x5	Rotation	Pitch	Positive rotation about positive Y-axis, following right hand rule.
6	x6	Rotation	Yaw	Positive rotation about positive Z-axis, following right hand rule.

# Body Centered Coordinate System
All vessel motions refer to the body coordinate system when at rest. The coordinate system does not move with the body. All reported motions are relative to a static coordinate system. This imposes the following assumptions:
## Assumptions
Vessel motions are small, relative to body initial position.
# Converting Vessel Motions Between Global and Body Coordinate Systems
Before solving for vessel motions, oFreq first converts all body forces into the global coordinate system. Body motions are solved, and then converted back into the body coordinate system. The following equations show the exact conversion formula that oFreq uses.
The conversion changes, depending on the specific motion model used. The exact conversion matrix is encoded within each motion model. Thankfully, regardless of the exact derivation for the conversion matrix, it always gets used in the same manner. The following sections show how to use the conversion matrix to convert between global and body coordinates for each major item used in motion analysis.
## Converting Forces and Moments
Forces and moments can be considered a vector, just like position. Because of this relationship, the coordinate transform for position also applies to all forces and moments. The only extra feature is that the offset of the coordinate origin means there is a coupling between forces and moments. This results in a conversion matrix that combines forces and moments between coordinate systems.

### Converting From Global to Body Forces
Equation 3.1 shows use of the the conversion matrix from global to body coordinates. The equation assumes a six degree of freedom model, but the same concept can be applied to any motion model. In all cases, the conversion matrix is premultiplied to the force matrix.
left [ stack { F_x # F_y # F_z # M_x # M_y # M_z } right ] = [D] left [ stack { F_xG # F_yG # F_zG # M_xG # M_yG # M_zG } right ]
Equation 3.1
Variables:
[D] =	Full conversion matrix.
FxG =	Force along the X-axis, global coordinate system.
FyG =	Force along the Y-axis, global coordinate system.
FzG =	Force along the Z-axis, global coordinate system.
MxG =	Moment about the X-axis, global coordinate system.
MyG =	Moment about the Y-axis, global coordinate system.
MzG =	Moment about the Z-axis, global coordinate system.
FxG =	Force along the X-axis, body coordinate system.
FyG =	Force along the Y-axis, body coordinate system.
FzG =	Force along the Z-axis, body coordinate system.
MxG =	Moment about the X-axis, body coordinate system.
MyG =	Moment about the Y-axis, body coordinate system.
MzG =	Moment about the Z-axis, body coordinate system.
### Converting From Body to Global Forces
Converting from body to global coordinates requires the inverse of the conversion matrix. Because the matrix is orthogonal, the inverse simply equals the transpose of the conversion matrix. The inverse conversion matrix is used to convert from body forces back to global forces. (Equation 3.2)
left [ stack { F_Gx # F_Gy # F_Gz # M_Gx # M_Gy # M_Gz } right ] = [D]^-1 left [ stack { F_x # F_y # F_z # M_x # M_y # M_z } right ]
Equation 3.2
## Converting Motions
Body motions are also a vector property, just like forces and moments. Body motions also have translation and rotation components, just like forces and moments. The exact same conversion matrix applied to forces and moments can also be used to convert motions from global to body coordinates.
### Converting from Global to Body Motions
Equation 3.3 defines the full conversion matrix that will convert from global motions to body motions. This example assumes a six degree of freedom motion model.
left [ stack { x_1 # x_2 # x_3 # x_4 # x_5 # x_6 } right ] = [D] left [ stack { x_1G # x_2G # x_3G # x_4G # x_5G # x_6G } right ]
Equation 3.3
Variables:
x1 =	Translation in the X-axis, body coordinate system.
x2 =	Translation in the Y-axis, body coordinate system.
x3 =	Translation in the Z-axis, body coordinate system.
x4 =	Rotation about the X-axis, body coordinate system.
x5 =	Rotation about the Y-axis, body coordinate system.
x6 =	Rotation about the Z-axis, body coordinate system.
x1B =	Translation in the X-axis, global coordinate system.
x2B =	Translation in the Y-axis, global coordinate system.
x3B =	Translation in the Z-axis, global coordinate system.
x4B =	Rotation about the X-axis, global coordinate system.
x5B =	Rotation about the Y-axis, global coordinate system.
x6B =	Rotation about the Z-axis, global coordinate system.
### Converting From Body To Global Motions
Just like with the body forces, the inverse conversion matrix can be used to convert from body motions to global motions.
left [ stack { x_1G # x_2G # x_3G # x_4G # x_5G # x_6G } right ] = [D]^-1 left [ stack { x_1 # x_2 # x_3 # x_4 # x_5 # x_6 } right ]
Equation 3.4
Variables:
x1 =	Translation in the X-axis, body coordinate system.
x2 =	Translation in the Y-axis, body coordinate system.
x3 =	Translation in the Z-axis, body coordinate system.
x4 =	Rotation about the X-axis, body coordinate system.
x5 =	Rotation about the Y-axis, body coordinate system.
x6 =	Rotation about the Z-axis, body coordinate system.
x1B =	Translation in the X-axis, global coordinate system.
x2B =	Translation in the Y-axis, global coordinate system.
x3B =	Translation in the Z-axis, global coordinate system.
x4B =	Rotation about the X-axis, global coordinate system.
x5B =	Rotation about the Y-axis, global coordinate system.
x6B =	Rotation about the Z-axis, global coordinate system.
## Conversion of Velocity and Acceleration
Conversion of coordinate systems for velocity and acceleration is not necessary. The body motions are calculated in the global coordinate system and then immediately converted back to the body coordinate system. All accelerations and velocities are then derived from the motions in the body coordinate system.
# Derivation of Conversion Matrix
The exact mathematics for the conversion matrix depend on the motion model used. The formula for conversion are encoded within each motion model as another set of equations. Full derivations are provided for each motion model. However, it is illustrative to show this derivation in the current page to understand how the conversion matrix interacts with the combinations of translation and rotation motions.
For this derivation, we assume a six degree of freedom motion model. Previous work demonstrated that this conversion matrix can be applied to any vector quantity. For these derivation purposes, we shall only use generic motions as the example situation. The conversion from global to body coordinates is the combination of the coordinate transform matrix, and a coupling matrix between translation and rotation.
left [ stack { X_x # X_y # X_z # R_x # R_y # R_z } right ] = left [ matrix { [T] # [C] ## [C]^-1 # [T] } right ] left [ stack { X_xG # X_yG # X_zG # R_xG # R_yG # R_zG } right ]
Equation 4.1
Variables:
[T] =	Coordinate transformation matrix.
[C] =	Coupling matrix between translation and rotation.
XxG =	Translation motion in the X-axis, global coordinate system.
XyG =	Translation motion in the Y-axis, global coordinate system.
XzG =	Translation motion in the Z-axis, global coordinate system.
RxG =	Rotation motion about the X-axis, global coordinate system.
RyG =	Rotation motion about the Y-axis, global coordinate system.
RzG =	Rotation motion about the Z-axis, global coordinate system.
Xx =	Translation motion in the X-axis, body coordinate system.
Xy =	Translation motion in the Y-axis, body coordinate system.
Xz =	Translation motion in the Z-axis, body coordinate system.
Rx =	Rotation motion about the X-axis, body coordinate system.
Ry =	Rotation motion about the Y-axis, body coordinate system.
Rz =	Rotation motion about the Z-axis, body coordinate system.

Equation 4.2 defines the coupling matrix.
left [ C right ] = left [ matrix { 0 # -P_z # P_y ## P_z # 0 # -P_x ## -P_y # P_x # 0 } right ]
Equation 4.2
Variables:
Px =	Offset from global coordinate origin to body coordinate origin, along X-axis.
Py =	Offset from global coordinate origin to body coordinate origin, along Y-axis.
Pz =	Offset from global coordinate origin to body coordinate origin, along Z-axis.

This coupling matrix can be used to convert from translation to rotation components (motions, or convert forces to moments).
[R] = [C] [X]
Equation 4.3
Variables:
[R] =	Generic matrix for rotation components (X, Y, Z axis).
[X] =	Generic matrix for translation components (X, Y, Z axis).

The inverse matrix can be used to convert from rotation to translation components. Because the matrix is orthogonal, the transpose is the inverse of the matrix. (Equation 4.4)
[C]^-1 = [C]^T = left [ matrix { 0 # P_z # -P_y ## -P_z # 0 # P_x ## P_y # -P_x # 0 } right ]
Equation 4.4

The inverse coupling matrix can be used to convert from moments back to forces. (Equation 4.5)
[F] = [C]^T [M]
Equation 4.5

The coupling matrix and coordinate transform matrix can be combined to form the full conversion matrix between global and body coordinates. The following sections show the full application of the conversion matrix.
## Converting from Global to Body Coordinates
Equation 4.6 shows the fully expanded matrix to convert from global coordinate to body coordinates. This is the expanded result of combining the coordinate transform matrix and the coupling matrix.
[D] = left [ matrix { cos(%alpha) # sin(%alpha) # 0 # 0 # -P_z # P_y ## -sin(%alpha) # cos(%alpha) # 0 # P_z # 0 # -P_x ## 0 # 0 # 1 # -P_y # P_x # 0 ## 0 # P_z # -P_y # cos(%alpha) # sin(%alpha) # 0 ## -P_z # 0 # P_x # -sin(%alpha) # cos(%alpha) # 0 ## P_y # -P_x # 0 # 0 # 0 # 1} right ]
Equation 4.6
This can be used to convert motions from global to body coordinates, following Equation 3.3.

## Converting from Body to Global Coordinates
To convert from body to global coordinates, we need the inverse matrix of Equation 4.6. Thankfully, this matrix is orthogonal and the inverse is simply the transpose of the original conversion matrix. Error: Reference source not found shows the resulting inverted matrix, which converts from body to global coordinates.
[D]^-1 = [D]^T = left [ matrix { cos(%alpha) # -sin(%alpha) # 0 # 0 # P_z # -P_y ## sin(%alpha) # cos(%alpha) # 0 # -P_z # 0 # P_x ## 0 # 0 # 1 # P_y # -P_x # 0 ## 0 # -P_z # P_y # cos(%alpha) # -sin(%alpha) # 0 ## P_z # 0 # -P_x # sin(%alpha) # cos(%alpha) # 0 ## -P_y # P_x # 0 # 0 # 0 # 1} right ]
Equation 4.7
This can be used to convert motions from global to body coordinates, following Equation 3.4.