Bodies
# Overview
The body represents a single floating object on the ocean. The body contains all the inputs for the different force terms which affect it. It also records the final calculated motions for that body.
# Coordinate System
All references within the body are within the body coordinate system. See the page on body coordinate systems for further information.
# Body Mass
The body mass definition assumes a six-degree of freedom rigid body. The user provides based inputs such as mass, center of gravity, and the moments of inertia in each axis. The body uses that information to calculate and record an internal mass matrix. This mass matrix is used by by any motion models that reference the ForceMass() function. Equation 3.1 shows the mass matrix definition.
left [ M right ] = left [ matrix { M # 0 # 0 # 0 # +M z_g # -M y_g ## 0 # M # 0 # -M z_g # 0 # +M x_g ## 0 # 0 # M # +M y_g # -M x_g # 0 ## 0 # -M z_g # +M y_g # I_xx # -I_xy # -I_xz ## +M z_g # 0 # -M x_g # -I_xy # I_yy # -I_yz ## -M y_g # +M x_g # 0 # -I_xz # -I_yz # I_zz } right ]
Equation 3.1
Variables:
M =	Body mass.
xg =	Body center of gravity, X-axis (body coordinate system).
yg =	Body center of gravity, Y-axis (body coordinate system).
zg =	Body center of gravity, Z-axis (body coordinate system).
Ixx =	2nd moment of inertia, X-axis.
Iyy =	2nd moment of inertia, Y-axis.
Izz =	2nd moment of inertia, Z-axis.
Ixy =	Cross product of inertia, XY-axis.
Ixz =	Cross product of inertia, XZ-axis.
Iyz =	Cross product of inertia, YZ-axis.

## Simulating Additional Mass Terms
The body mass definition only includes the variables and equations expected for a normal six degree of freedom rigid body. You can use motion models that only select a subset of these motions. But if your motion model required mass items beyond variable 6, then you will need to simulate the additional mass terms.
The body mass is really just a reactive force object that depends on the second order derivative of body motions. You can simulate additional mass terms by creating your own ForceReact_user force whose coefficients all depend on the second order derivative. This is identical to the behavior expected if the body mass did include your additional terms.
# Body Forces
The following forces are available for each body object.
In oFreq, the forces are defined separate from the body, and then each body references the forces. So if you change a force definition, it will change for all bodies that reference that force.
## Mass Forces
There is only one ForceMass object per body. This gets automatically defined when you define the mass properties. At a minimum, the mass must be defined for each body. Other properties for rotational moment of inertia can be included as needed for each individual analysis.
## Reactive Forces
Reactive forces depend on body motions. A single ForceReact object can contain inputs defined for multiple derivatives. Each derivative allows input definitions for each equation and variable. This allows maximum flexibility for definition of ForceReact objects. All the different derivatives associated with a force can be grouped under one object. There are two different types of ForceReact forces.
1. ForceReact_user
2. ForceReact_hyro
### ForceReact_user: User Reactive Forces
User reactive forces are defined by the user. These can contain any order of derivative from 0 to infinity. Most applications will only include derivatives up to 2nd order. But the flexibility allows for exotic implications. For example, the dynamics of a reactive control system could be programmed as a reactive force.
### ForceReact_hydro: Hydrodynamic Reactive Forces
Hydrodynamic reactive forces come from hydrodynamic interactions of the body motions with calm water. (Effects of incident waves are included in a separate force). Whenever you specify a name for the hydrodynamic body, oFreq automatically retrieves the data for the hydrodynamic forces. Only one hydrodynamic force is defined for each body. The following terms are included in a hydrodynamic force.
### Added Mass
This term varies with the second order derivative of body motions. You can learn more about it under the section on hydrodynamic coefficients.
AddedMass approx {d^2 underline x} over dt^2
Equation 4.1
Variables:
x =	Generic variable for vessel motion.
t =	Time.
### Added Damping
This term varies with the first order derivative of body motions. You can learn more about it under the section on hydrodynamic coefficients.
AddedDamping approx {d underline x} over dt
Equation 4.2
Variables:
x =	Generic variable for vessel motion.
t =	Time.
### Hydrostatic Stiffness
This term varies with the zero order derivative of body motions. The hydrostatic stiffness only applies to a few specific body motions. You can learn more about it under the section on hydrodynamic coefficients.
#### Heave Stiffness
F_h3 approx x_3
Equation 4.3
Variables:
Fh3 =	Force of hydrodynamic stiffness due to body translation in the Z-axis (body coordinate system).
x3 =	Body translation in the Z-axis (body coordinate system).

#### Roll Stiffness
F_h4 approx x_4
Equation 4.4
Variables:
Fh4 =	Force of hydrodynamic stiffness due to body rotation about the X-axis (body coordinate system).
x4 =	Body rotation about the X-axis (body coordinate system).
#### Pitch Stiffness
F_h5 approx x_5
Equation 4.5
Variables:
Fh5 =	Force of hydrodynamic stiffness due to body rotation about the Y-axis (body coordinate system).
x5 =	Body rotation about the Y-axis (body coordinate system).

## Crossbody Forces
The crossbody forces work exactly the same as a reactive force, except that the forces produced depend on the motions of another body. The body is not even specified during force definition. You actually specify the sending body when you reference the force in the definition of the receiving body.
1. Sending body: The body whose motions generate the crossbody force.
2. Receiving body: The body which actually receives the forces generated.

Crossbody forces are not necessarily symmetric. oFreq will allow you to generate a body that only receives a crossbody force and does not send any forces of its own.
Defining a body that only receives crossbody forces will violate Newton's third law of motion for every scenario the author can conceive. For every force, there must be an equal and opposite force. So, for every body that receives a crossbody force, the same body must also send a crossbody force. But,. if you have a scenario that requires a one-sided crossbody force definition, oFreq will faithfully solve for it.
Just like with reactive forces, there are two types of crossbody forces:
1. ForceCross_user
2. ForceCross_hydro
### ForceCross_user: User Crossbody Forces
These are defined exactly the same as a user reactive force.
### ForceCross_hydro: Hydrodynamic Crossbody Forces
Just like hydrodynamic reactive forces, these are defined automatically when you specify a hydrobody. The hydrodynamic crossbody forces will only model added damping and added mass, as there is no hydrostatic interaction between bodies.
### Crossbody Added Mass
This term varies with the second order derivative of body motions of the sending body. You can learn more about it under the section on hydrodynamic coefficients.
AddedMass approx {d^2 underline x_b} over dt^2
Equation 4.6
Variables:
x =	Generic variable for vessel motion.
t =	Time.
b =	index of the body sending the crossbody force.
### Crossbody Added Damping
This term varies with the first order derivative of body motions. You can learn more about it under the section on hydrodynamic coefficients.
AddedDamping approx {d underline x_b} over dt
Equation 4.7
Variables:
x =	Generic variable for vessel motion.
t =	Time.
b =	index of the body sending the crossbody force.
## Active Forces
The active forces are force terms that do not depend on body motions. They are oscillating forces, but have a constant amplitude. These forces are defined as complex input coefficients. The complex number allows the user to also specify a phase angle for the force. There are two types of active forces.
1. ForceActive_user
2. ForceActive_hydro
### ForceActive_user: User Active Forces
User active forces are defined by the user. There can only be one coefficient for each equation specified. However, you can define an unlimited number of active force objects.
### ForceActive_hydro: Hydrodynamic Active Forces
The hydrodynamic active forces are automatically defined when you specify a hydrobody. There are two hydrodynamic active forces for each body: forces from incident waves; and forces from diffracted waves. The total excitation forces results from the sum of incident and diffracted forces.
The phase angles that result from the hydrodynamic active forces are the phase angle in relation to the incident waves.
# Body Coordinate Systems
Each body has its own coordinate system. This coordinate system remains oriented to the body. When you change the body heading, the body coordinate system changes to match the new heading. Any specifications to the body, such as the center of gravity, are done in the body coordinate system. Any resulting body motions or forces are in the body coordinate system.
# Multibody Support
oFreq supports multiple bodies. Each body is defined separately. Each body has its own coordinate system. Unless crossbody forces are included, the bodies have no interactions with each other.
## Crossbody Forces coordinate systems
Crossbody forces can still be specified in the body coordinate systems. When oFreq solves for body motions, it first converts all forces back into the global coordinate system. When the crossbody force gets converted, oFreq will apply the heading of the receiving body to resolve any rotation of coordinate systems.