Body Static Acceleration
# Result
This output provides information about the body static acceleration. The body static acceleration results from static gravity. Normally, static gravity pulls vertically down, in a global coordinate system. However, the rotational motions of the body mean that during the extreme of the motion, static gravity has strong sideways components in the body coordinate system. The exact magnitude of sideways component depends on the amplitude of the body rotation motions. These motions depend on wave frequency.
The output provides variation of the acceleration due to static gravity as a sideways component. This may be combined with local acceleration values to obtain the total design acceleration at a given point on the body. All measurements are in the body coordinate system.
## Units of Measurement
The units of static acceleration are meters per second squared (m/s2).
units = m / s^2
Equation 1.1
Variables:
m =	Units of meters (m).
s =	Units of seconds (s).
# Assumptions / Limitations
This output makes the following assumptions.
1. This outputs assumes rigid body motion.
2. This output assumes an oscillatory motion at a steady state value. Transient effects are ignored.
3. This output assumes a standard six degree of freedom motion model (6DOF). The output will still calculate if not all of the 6DOF variables are included, but that will affect the final solution. And the output can not consider any motion variables that extend beyond rigid body motion (the reserved variables of 1 – 6).
4. Body motions are defined from the origin of the body coordinate system.
5. Normal earth gravity is assumed to be 9.8065 m/s2, directed vertically down (negative Z-axis in the global coordinate system.)
# Variable Dependencies
This output depends on the following variables.
1. Body encounter frequency.
2. Global wave direction.
3. Body heading.
4. All the body input forces
5. Global wave spectrum
6. Position specified for the local solution.
# Derivation
The static acceleration has three components:
1. X-axis component, body coordinate system.
2. Y-axis component, body coordinate system.
3. Z-axis component, body coordinate system.
The X-axis and Y-axis components report the maximum static acceleration, from the extreme of ship rotation. The Z-axis component reports the minimum static acceleration, also from the extreme of ship acceleration. The following derivations demonstrate this.
## X-axis Static Acceleration
The X-axis static acceleration originates from body pitch motion, rotation about the Y-axis, body coordinate system. (Equation 4.1)
a_x = g sin left ( Re left lbrace underline X_5 right rbrace right )
Equation 4.1
Variables:
g =	Static acceleration due to Earth gravity (9.8065 m/s2).
X5 =	Amplitude of body motion variable, index 5 (pitch motion).
underline notation denotes a complex number.

## Y-axis Static Acceleration
The Y-axis static acceleration originates from body roll motion, rotation about the X-axis, body coordinate system. (Equation 4.2)
a_y = -g sin left ( Re left lbrace underline X_4 right rbrace right )
Equation 4.2
Variables:
g =	Static acceleration due to Earth gravity (9.8065 m/s2).
X4 =	Amplitude of body motion variable, index 4 (roll motion).
underline notation denotes a complex number.

## Z-axis Static Acceleration
The Z-axis static acceleration originates from the combination of both body pitch motion, rotation about the Y-axis, and body roll motion, rotation about the X-axis. All motions are in body coordinate system. The following equation shows the minimum vertical component of static acceleration. The maximum is still a value of g (9.8065 m/s2). (Equation 4.3)
a_z = g left [ cos left ( Re left lbrace underline X_5 right rbrace right ) cdot cos left ( Re left lbrace underline X_4 right rbrace right ) right ]
Equation 4.3
Variables:
g =	Static acceleration due to Earth gravity (9.8065 m/s2).
X5 =	Amplitude of body motion variable, index 5 (pitch motion).
underline notation denotes a complex number.
Although the body static acceleration is based on encounter frequency, it can still be compared to the global wave frequency. The dependency is a valid comparison.
But do not extend this concept to the response amplitude operators. The calculation of the RAO depends on the exact encountered wave spectrum and can not be generalized to the global wave frequency.
# Application to Custom Motion Models
This output assumes a standard six degree of freedom motion model (6DOF). The output will still calculate if not all of the 6DOF variables are included, but that will affect the final solution. And the output can not consider any motion variables that extend beyond rigid body motion (the reserved variables of 1 – 6).
This output will still work with custom motion models, but it can only access information for motion variables 1 – 6. These outputs are reserved for rigid body motions. If you require static acceleration information that includes the effects of other custom motion variables, this output will not return an accurate solution. Consider developing a custom output.
# Response Amplitude Operator (RAO)
Most of the outputs are presented in two formats: the absolute value, and a response amplitude operator (RAO). The RAO gives the relative output for the given input. This can be useful when comparing the performance of the body on a general basis, independent of the given seastate. However, calculation of an RAO is not consistent through the industry or even from one input to the next. Section 6 addresses this by describing the exact calculation method of the RAO for each output.
## RAO Calculation
The RAO calculation is divided into two sections: first the RAO normalization is derived; and then the actual method of RAO application is shown. This may be specific to each RAO.
### RAO Normalization
For all static acceleration variables, the RAO is normalized based on wave amplitude for the given body encounter spectrum. (Equation 6.1)
RAO(a_i) = a_i over %zeta_0b
Equation 6.1
Variables:
ζ0b =	Encountered wave amplitude for the body of index b.
i =	Index of which static acceleration variable is requested (i = x, y, or z)
ai =	Body static acceleration for index i.
### RAO Application
The RAO can be applied with simply multiplying by the wave amplitude.
a_i = RAO(a_i) %zeta_0b
Equation 6.2
Variables:
ζ0b =	Encountered wave amplitude for the body of index b.
RAO(ai) =	Response amplitude operator to convert from body wave amplitude to body static acceleration, for index i.
i =	Index of which static acceleration variable is requested (i = x, y, or z)

Sometimes, it is more convenient to apply the RAO directly to the wave energy spectrum. There are two wave energy spectra to select from: the body encounter spectrum, and the global wave spectrum. Error: Reference source not found shows application of the global wave spectrum. This includes application of an additional RAO to convert from the global wave spectrum to the body encounter spectrum. The output from this calculation is the spectral energy density for the acceleration of the local solution.
S left ( a_i right ) = left ( RAO(a_i) right )^2 cdot left [ RAO left ( S ( %omega_G) right ) cdot S(%omega_G) right ]
Equation 6.3
Variables:
RAO(ai) =	Response amplitude operator to convert from body wave amplitude to body static acceleration, for index i.
RAO(S(%omega_G)) = ~	RAO to convert from global wave spectrum to body encountered spectrum.
S(ωG) =	Global wave spectrum, spectral energy density.
## RAO Units
The units of the resulting RAO output can become very confusing, depending on how the RAO gets calculated. This section clarifies by clearly stating the units for each RAO.
The units for local static acceleration are s-2. (Equation 6.4)
left [ RAO left ( a_i right ) right ]_units = m over {m s^2} = 1 over s^2 = s^-2
Equation 6.4
Variables:
m =	Units of meters (m).
s =	Units of seconds (s).