6DOF Motion Model
# Introduction
The six degree of freedom (6DOF) motion model includes all six degrees of freedom for a rigid body. This is the most common model for dynamics solvers. Common applications include:
1. Vessels in a seaway
2. Small boats or objects stationary in a seaway
3. Buoy motions.

The 6DOF model includes the full level of detail. It is the most accurate of the standard motion models included in oFreq. However, because of this accuracy, it also requires the most data for accurate input values. Standard hydrodynamic coefficients from a robust radiation-diffraction solver should supply data for all six degrees of freedom. Additional information will be required, such as ship mass and mass moment of inertia.
If you do not have reliable data for all motions, consider using a more simplistic motion model. Remember that all equations interact with each other. Unreliable data in one equation could lead to large errors in other equations.
The 6DOF model has six equations and six variables. The variables are:
1. TX = x0: Translation in the X-axis (m).
2. TY = x1: Translation in the Y-axis (m).
3. TZ = x2: Translation in the Z-axis (m).
4. RX = x3: Rotation about the X-axis (rad).
5. RY = x4: Rotation about the Y-axis (rad).
6. RZ = x5: Rotation about the Z-axis (rad).

The equation indexes are:
1. TX = x0: Translation in the X-axis (m).
2. TY = x1: Translation in the Y-axis (m).
3. TZ = x2: Translation in the Z-axis (m).
4. RX = x3: Rotation about the X-axis (rad).
5. RY = x4: Rotation about the Y-axis (rad).
6. RZ = x5: Rotation about the Z-axis (rad).
# General Equation Context
The 6DOF model involves repetition of a basic concept for six different equations. The following equations shows the generic concept equation.
Mass + Origin Offset Terms + ~ newline sum from derivative left ( sum from {motion variable} Hydrodynamic Reactive Forces right ) + ~ newline sum from derivative left ( sum from {motion variable} User Reactive Forces right ) + ~ newline sum from bodies left [ sum from derivative left ( sum from {motion variable} Hydrodynamic Crossbody Forces right ) right ] + ~ newline sum from bodies left [ sum from derivative left ( sum from {motion variable} User Crossbody Forces right ) right ] + ~ newline newline ~ = ~ newline newline Hydrodynamic Active Force + ~ newline User Active Force
Equation 2.1

# Included Forces
The 6DOF model includes all components for the following force types.
1. ForceMass()
2. Reactive Forces
  1. ForceReact_user()
  2. ForceReact_hydro()
3. Crossbody Forces
  1. ForceCross_user()
  2. FroceCross_hydro()
4. Active Forces
  1. ForceActive_user()
  2. ForceActive_hydro()
# Derivative Support
The model supports derivatives of hydrodynamic forces, from an order of 0 to a 2nd order derivative. This includes the following hydrodynamic forces:
1. Hydrostatic restoring force (0th order derivative)
2. Added damping (1st order derivative)
3. Added mass (2nd order derivative)
# Multibody Support
The model includes full multibody support. All crossbody forces are supported. The model can accommodate an unlimited number of bodies, with full force interaction through crossbody forces between all bodies, if necessary.