Data Retrieval Functions
# Introduction
The main set of functions work for data retrieval. Each of these functions retrieves the user inputs for a specific type of force. You can find definitions of the different force types in the definitions section.
## Data Retrieval Method
Be aware that oFreq allows the user to define multiple instances of each force type. These data retrieval functions will automatically return the total sum from all defined instances. When programming the motion model, you do not need to worry about combining multiple force definitions. oFreq automatically handles that, including correctly matching all variables and derivatives.
For example. Say a user defined two ForceActive_user forces.
Table 1.1: Example Defined Forces
Force	Coefficient	Variable
Force1	3.0 + 5j	var1
Force2	-1 + 2j	var1

In this case, the ForceActive_user(1) function would return a value of (2.0 + 7j), which is the sum of coefficients for both forces. (The value of 1 was entered as an argument to the function. This specified to return the values for variable 1.) Take one more example where the two forces have coefficients defined for different variables.
Table 1.2: Example Defined Forces – Multiple Variables
Force	Coefficient	Variable
Force1	3.0 + 5j	var1
Force2	-1 + 2j	var2

In this case, the ForceActive_user(1) function returns just the value of var1 (3.0 + 5j). This was because the argument to the function asked for the values of var1. Force2 did not have any inputs that qualified.
 The following sections list simple descriptions for the data retrieval functions available in oFreq.
# ForceMass() Function
The forces associated with the mass of an object. This includes direct mass for straight linear motion, and moment of inertia for rotational motion. This also includes any forces due to the mass being off center from the point of rotation. All these properties are defined when you enter the mass properties for the body.
The origin of the body coordinate system is assumed as the point of rotation.
## Syntax
The following example shows the syntax for implementing the ForceMass() function.
ForceMass( varIn)
## Parameters
Table 2.1 lists the input parameters.
Table 2.1: Input Parameters
Parameter / Name	Valid / Range	Description
		No equation index is required. The function automatically determined the equation index based on which equation it was defined in.
varIn	Only indexes of motion variables.	The index of the variable requested.

# ForceActive_hydro() Function
The forces which are independent of body motions. The hydro subcategory refers to active forces that specifically come from hydrodynamic interactions. This includes the forces from incident waves. Sometimes call the Froude-Krylov forces.
Note that the active force may be a constant, but it still does assume an oscillating force.
## Syntax
The following example shows the syntax for implementing the ForceActive_hydro() function.
ForceActive_hydro()
## Parameters
Table 3.1 lists the input parameters. This function has no input parameters. The table was included to show that it still takes on implied input parameter from the equation of motion.
Table 3.1: Input Parameters
Parameter / Name	Valid / Range	Description
		No equation index is required. The function automatically determined the equation index based on which equation it was defined in.

# ForceActive_user() Function
The forces which are independent of body motions. The user subcategory refers to active forces that specifically come from user defined interactions. Some examples may include:
1. Large, out of balance machinery.
2. Thrusters pulsing side to side.

Note that the active force may be a constant, but it still does assume an oscillating force.
## Syntax
The following example shows the syntax for implementing the ForceActive_user() function.
ForceActive_user()
## Parameters
Table 8.1 lists the input parameters. This function has no input parameters. The table was included to show that it still takes on implied input parameter from the equation of motion.
Table 4.1: Input Parameters
Parameter / Name	Valid / Range	Description
		No equation index is required. The function automatically determined the equation index based on which equation it was defined in.

# ForceReact_hydro() Function
The forces which are reactive and dependent on body motions. This includes derivatives of body motions. The hydro subcategory refers to reactive forces hydrodynamic in origin. This would include body hydrostatic properties, added damping, and added mass.
Forces in this category only depend on the 0th to 2nd order derivatives of vessel motions.
## Syntax
The following example shows the syntax for implementing the ForceReact_hydro() function.
ForceReact_hydro(ordIn, varIn)
## Parameters
Table 8.1 lists the input parameters.
Table 5.1: Input Parameters
Parameter / Name	Valid / Range	Description
		No equation index is required. The function automatically determined the equation index based on which equation it was defined in.
ordIn	0 to 2	Selects the order of derivative for the force.
varIn	Only indexes of motion variables.	The index of the variable requested.

# ForceReact_user() Function
The forces which are reactive and dependent on body motions. This includes derivatives of body motions. The user subcategory refers to reactive forces defined by the user. Examples include:
1. Vessel control system
2. Vessel mooring lines
3. Anti-Roll tanks
4. Shifting of loose weights.

Forces in this category depend on the 0th to Nth order derivatives of vessel motions. The derivatives are not restricted for this category. oFreq will automatically include any reactive forces defined for any order of derivative.
## Syntax
The following example shows the syntax for implementing the ForceReact_user() function.
ForceReact_user(ordIn, varIn)
## Parameters
Table 8.1 lists the input parameters.
Table 6.1: Input Parameters
Parameter / Name	Valid / Range	Description
		No equation index is required. The function automatically determined the equation index based on which equation it was defined in.
ordIn	0 to maximum order of derivative for user defined force.	Selects the order of derivative for the force.
varIn	Only indexes of motion variables.	The index of the variable requested.

# ForceCross_hydro() Function
The forces which are reactive and dependent on the body motions of another body. This is only applicable to multibody systems. One situation might be two vessels near each other during underway refueling. The hydro subcategory refers to reactive forces hydrodynamic in origin. Examples include:
1. body hydrostatic properties
2. added damping
3. added mass
Except all these forces would be dependent on the motions of another body.
This function only has any meaning in multibody situation. For single body situations, it will always evaluate to zero. However, you can use motion models which contain ForceCross terms and apply the model to single body problem. This does not jeopardize the program in any way.
Forces in this category only depend on the 0th to 2nd order derivatives of vessel motions. The derivatives are applied to the motions of another body. The other body is not required to have the same motion model.
Bodies can have different motion models and still interact.
It is possible for the function arguments to request the crossbody forces for the body interacting with itself. However, this request would have no meaning as self-interactions are stored under the ForceReact force functions. Any use of the ForceCross_hydro() function is usually coupled with the Kronecker delta function, which will exclude cases of self interaction.
## Syntax
The following example shows the syntax for implementing the ForceCross_hydro() function.
ForceCross_hydro(bodIn, ordIn, varIn)
## Parameters
Table 7.1 lists the input parameters.
Table 7.1: Input Parameters
Parameter / Name	Valid / Range	Description
		No equation index is required. The function automatically determined the equation index based on which equation it was defined in.
bodIn	1 to number of bodies	The index of the body requested.
ordIn	0 to 2	Selects the order of derivative for the force.
varIn	Only indexes of motion variables.	The index of the variable requested.

# ForceCross_user() Function
The forces which are reactive and dependent on the body motions of another body. This is only applicable to multibody systems. One situation might be two vessels near each other during underway refueling. The user subcategory refers to reactive forces defined by the user. Examples include:
1. Mooring lines between vessels
2. Interacting exhaust plumes
3. Any masses suspended from both vessels
Except all these forces would be dependent on the motions of another body.
This function only has any meaning in multibody situation. For single body situations, it will always evaluate to zero. However, you can use motion models which contain ForceCross terms and apply the model to single body problem. This does not jeopardize the program in any way.
Forces in this category only depend on the 0th to Nth order derivatives of vessel motions. The derivatives are not restricted for this category. oFreq will automatically include any reactive forces defined for any order of derivative. The derivatives are applied to the motions of another body. The other body is not required to have the same motion model.
Bodies can have different motion models and still interact.
It is possible for the function arguments to request the crossbody forces for the body interacting with itself. However, this request would have no meaning as self-interactions are stored under the ForceReact force functions. Any use of the ForceCross_user() function is usually coupled with the Kronecker delta function, which will exclude cases of self interaction.
## Syntax
The following example shows the syntax for implementing the ForceCross_user() function.
ForceCross_user(bodIn, ordIn, varIn)
## Parameters
Table 8.1 lists the input parameters.
Table 8.1: Input Parameters
Parameter / Name	Valid / Range	Description
		No equation index is required. The function automatically determined the equation index based on which equation it was defined in.
bodIn	1 to number of bodies	The index of the body requested.
ordIn	0 to maximum order of derivative for user defined force.	Selects the order of derivative for the force.
varIn	Only indexes of motion variables.	The index of the variable requested.