Index Functions
# Introduction
Many of the data retrieval functions require you to specify the exact motion variable and exact derivative that you want the results for. But these numbers need to change when you include a data retrieval function inside a sum() function. The numbers must dynamically update with each iteration of the sum() function. To allow this, oFreq also provides several index functions. You can use these index functions as parameters for the data retrieval function, and oFreq automatically updates the index function with each iteration of the sum loop.
The index functions allow the user to develop dynamic specification for forces. They can also be combined with any other element of the equation of motion. This page lists all of the index functions available.
# Index Functions
## Body Index Functions
There are two functions to use for the body index.
### “body()” function
When you use the Sum() function to iterate through bodies, the different body indexes are reported in the body() function. Use this inside the data retrieval functions for forces.
The following example shows the syntax for implementing the function.
body();
### “curbody()” Function
The curbody() function reports the index for the current body. This is the body which is currently using the motion model that created this equation of motion. This is especially useful in multibody situations as you really have two body indexes to to consider. There is the index of the body you are currently working with (found from the curbody() function). And then there is the index of each of the other bodies (found from the body() function).
The following example shows the syntax for implementing the function.
curbody();
Both the curbody() and body() functions do not have any error checks to prevent them matching indexes. They can both request a body of the same index, and frequently do in most seakeeping equations of motion. Use the Kronecker delta function to appropriately handle scenarios where these two functions return the same index.
## Derivative Index Functions
### “ord()” function
The ord() function returns the value of the current order of derivative. This is both the order of the derivative, and the index used to store information specific to that derivative.
The following example shows the syntax for implementing the function.
curbody();
## Variable Index Functions
### “var()” Function
The var() function returns the value of the current variable of motion. Be careful in handling summations. When summing terms, the var() function iterates sequentially and continuously from the minimum to the maximum variable of motion. Except the indexes for your variables of motion may not be continuous or sequential. For example, you can easily define a motion model with the following variable indexes:
- 1: Translation X-axis.
- 5: Rotation Y-axis.
- 3: Translation Z-axis.
- 10: Custom variable of motion.
The var() function would still return all the values between 1 and 10. The data retrieval functions have a safeguard to simply return a value of zero for any request that is beyond the data they contain. Just remember to include similar safeguards in any custom functions you may program.
## Equation Index Functions
No function is required for the index of the equation of motion. Remember that all your equations are defined within an equation of motion object. That object has the equation index set as one of its properties. All the data retrieval functions know this and automatically get the equation index from the equation of motion object.
# Limit Functions
In addition to the actual index functions, there are also functions which report the limits of iteration for each index variable.
## Body Limit Functions
### Lower Limit Function
No lower limit function is required. The bodies always start numbering from body 1. The lowest index number is always 1.
### “maxbod()” Upper Limit Function
The maxbod() function reports the maximum index of bodies included in the analysis.
## Derivative Limit Functions
### Lower Limit Function
No lower limit function is required. The derivatives always start numbering from an order of 0. The lowest index number is always 0.
### “maxord()” Upper Limit Function
The maxord() function reports the maximum order of derivative included in the analysis. This is the maximum from all the following force types:
1. ForceReact_user()
2. ForceReact_hydro()
3. ForceCross_user()
4. ForceCross_hydro()
5. ForceMass
## Variable Limit Functions
### “minvar()” Lower Limit Function
The minvar() function reports the lower limit of the motion variable index. It does not define if the space between the min and max limit is full of continuous motion variables. There may be missing motion variables. Plan effective error handling for this situation.
### “maxvar()” Upper Limit Function
The maxvar() function reports the upper limit of the motion variable index. It does not define if the space between the min and max limit is full of continuous motion variables. There may be missing motion variables. Plan effective error handling for this situation.