Data.in Input File
# Introduction
The “data.in” file contains reference to the data files associated with a body. A hydrobody gets defined. This definition includes the path to one or more oHydro run directories. oFreq then searches through those directories to find the appropriate output files and store that hydrodynamic data for use in the analysis.
Definition of a hydrobody does not require its use. You can create a library of relevant hydrobody files. The bodies.in input file specifies which hydrobody you want to use. Table 1.1 shows the relevant details for the file.
Table 1.1: Details of Data.In Input File
Folder:	Contained in the “constant” folder
Filename:	data.in
Instances:	There can only be one data file contained in any oFreq analysis.

# Organization
The headings in this document show the hierarchy of information, and that hierarchy matters.
1. Level 1 headings are used to organize general concepts. This does not reflect the actual organization used in the input files. (Example: 2 Organization)
2. Level 2 headings are used to specify objects for the input files. An object is a container that holds one or more keyword-value pairs. Anything within a class only applies to that class. This is the meaning of saying something has a scope of a given object. (Example: 2.1 Class Names)
  1. An object can also contain other sub-objects. This is called recursion. oFreq has no technical limits on the level of recursion, but the objects only have meaning for certain levels.
3. Level 3 headings specify keyword-value pairs. The heading is the keyword name. Specific information is given for the keyword, and the documentation describes the general use of the keyword.
## Object Names
The level 2 headings describe the objects and their names. There are two things you need to know about an object: the object name; and what the object does. All objects must be declared by their name. The rest is learning what each object does. Each level 2 heading includes descriptions of the object and its purpose.
All the major keywords for an object are also listed under that object. Sometimes, the same keyword might get used in multiple objects. In that case, it will still be listed under each relevant object, but some of the listings will only include a link to the section which contains the keyword-value pair description.
### Keyword Names
The keyword names list all the details. These are how you customize the objects and enter the information specific to your analysis. Every keyword-value entry includes a description, instructions on how to use it, at least one example, and a table like Table 4.1, which lists all the specific details for the keyword.
Table 2.1: Keyword Name Details
Scope:	This describes the scope of the keyword, which objects it can be used under. The full scope is always given like this: / object1::object2::keyword / This shows that some objects may be nested in other objects, showing you the full structure expected to correctly use this keyword. / If a keyword can be used in multiple objects, you will find multiple scopes listed.
Format:	Different keywords expect different formats for the input value. Some expect a text word, some expect complex numbers, etc. The exact format of input is listed here.
Valid Range:	Even if you get the format right, some keywords only like a specific range of values. Any restrictions are listed here.
Instances:	Describes how many times the keyword can be used within the scope of a single object. Some keywords allow multiple instances. Some only allow a single instance.
Required:	States whether the input is required, or if oFreq will assume a default value without any input.
Default Value:	If the input is not required, this is the default value that will be supplied when you do not supply the keyword-value pair. (You must leave out the entire keyword-value pair. Do not just enter the keyword and leave a value blank. That will produce an error.)
Dependents:	Some keywords also depend on other items being defined. Any dependencies are listed here. These may be another keyword, or another object.
Similar Keywords:	Many times, you can do the same job with another keyword-value pair. Any similar keywords are listed here. You do not need to learn about the other keywords, but they make your work easier.

Example:
Every keyword-value pair includes at least one example.

# Seafile Declaration
The “seafile” object is included in every single input file used in oFreq. It must be the first object declared. You can have comments before it, but the first real piece of input code must be the seafile declaration.
## “seafile” Object
The seafile object specifies basic information about the input file itself. It tells oFreq how to read the input file. For the moment, this information is not necessary. The input structure is simple enough that oFreq knows how to read all input files. But as the program grows, the input structure may become more complex, and this seafile object may become essential so that oFreq knows how to interpret the input file. For the current revision of oFreq, just assign the default values to keep oFreq happy.
### “version” keyword
The version keyword specifies which version of oFreq should be used to interpret the inputs. This allows backwards compatibility if the input interpretation ever changes from one version to the next. For the moment, just enter a value of 1.0. Table 4.2 lists the keyword details.
Table 3.1: “version” Details
Scope:	seafile::version
Format:	Decimal input (Example: 1.0)
Valid Range:	1.0
Instances:	1
Required:	Required
Default Value:	None
Dependents:	seafile::format / seafile::object
Similar Keywords:	None

Example:
version	1.0;

### “format” Keyword
The format keyword specifies the format of the input file. A value of “ascii” indicates ASCII text, with free flowing formatting. Other formats may become necessary, such as binary formats. This input provides flexibility for future expansion of oFreq. For the current revision, just enter a value of “ascii”. Table 2.1 lists the keyword details.
Table 3.2: “format” Details
Scope:	seafile::format
Format:	text input
Valid Range:	ascii
Instances:	1
Required:	Required
Default Value:	None
Dependents:	seafile::version / seafile::object
Similar Keywords:	None

Example:
format	ascii;

### “object” Keyword
The object keyword specifies which dictionary oFreq should use to interpret the file contents. oFreq contains an internal set of dictionaries that define appropriate actions for each keyword. It looks to the “object” keyword to first tell it which dictionary oFreq must use to interpret the content.
Table 3.1 lists the keyword details.
Table 3.3: “format” Details
Scope:	seafile::format
Format:	text input
Valid Range:	ascii
Instances:	1
Required:	Required
Default Value:	None
Dependents:	seafile::version / seafile::object
Similar Keywords:	None

This item does actually change at some points in oFreq. The output files each have their own object keyword. For output files, the object keyword specifies the type of output. But for input files, all inputs have the keyword of “dictionary”. This instructs oFreq to use its dictionary definitions for input files, and select the correct dictionary based on the filename. This is also why the filename must match exactly.
Example:
object	dictionary;

# Objects Specific to This Input File
The following objects are used to define the hydrodynamic data sources.
## “hydrobody” Object
A single hydrobody object is a definition of hydrodynamic data files, and a name to identify this object. You can have an unlimited number of hydrobody objects defined, but each object must have a unique “name” keyword.
### “name” keyword
The name keyword identifies this specific hydrobody that you defined. It allows you to reference the hydrobody by name in the bodies.in file. The name you use in the bodies.in file must exactly match the name you defined here. The name can have spaces in it, but it must be enclosed in quotation marks. Table 4.1 lists the keyword details.
Table 4.1: “name” Details
Scope:	hydrobody::name
Format:	Text input. Text can be surrounded by quotation marks. oFreq takes everything within the quotation marks as a single text string.
Valid Range:	Name can be any combination of ASCII characters, including spaces. If using spaces, the name must be enclosed in quotation marks.
Instances:	1
Required:	Required
Default Value:	None
Dependents:	None
Similar Keywords:	None

Example:
name “hydrobody 1”;
### “filelocation” Keyword
The filelocation keyword identifies the locations of the oHydro runs that should be used for the hydrodynamic data. This is a list of file paths. File paths can be relative or absolute. You can include spaces in the file path, but must enclose the path within quotation marks.
Table 4.2 lists the keyword details.
Table 4.2: “filelocation” Details
Scope:	hydrobody::filelocation
Format:	List input of text entries. Text can be surrounded by quotation marks. oFreq takes everything within the quotation marks as a single text string.
Valid Range:	Text must be file paths to root directory of oHydro run files. File path can be relative or absolute. / If running oFreq on MS Windows, use the Windows file path convention. This includes drive letters and back slashes ( \ ) for folder names. / If running oFreq on Linux, use the Linux file path convention. This includes forward slashes ( / ) for folder names.
Instances:	Single, but multiple entries within the list.
Required:	At least one entry in the list is required.
Default Value:	None
Dependents:	hydrobody::name
Similar Keywords:	None

The file path is specified to the root folder of the oHydro run. oFreq finds its own way to the relevant output files from there. The list of oHydro runs can include one or more locations. The oHydro run at each location should be based on a different incident wave amplitude. When you specify a list of oHydro locations, oFreq automatically interpolates between all data sets listed to find the closed match to the wave amplitude specified for the current wave frequency and direction.
Example:
  filelocation (
  "../ohydro1/"
  "../ohydro2/"
  "/home/jeff/Wave Analysis/ohydro3/"
  );